## Slide 1
GOES-16 ABI L2+ Land Surface Temperature Provisional PS-PVR
March 19th, 2018
GOES-R AWG
Yunyue Yu*,
Peng Yu+, Heshun Wang+, Yuhan Rao+
NOAA/NESDIS/STAR*
ESSIC/CICS-MD, UMD+

## Slide 2: Outline
Review of Beta Maturity
Product Quality Evaluation
  General approach
  Major Issues Remaining
Provisional Maturity Assessment
Path to Full Validation Maturity
  Issues
  PLPTs
  Risks
Summary and Recommendations

## Slide 3: Review of Beta Maturity
GOES-16 Land Surface Temperature L2 Product Provisional PS-PVR

## Slide 4: LST Product Background
LST is the instantaneous temperature of the earth “skin”
Emissivity-explicit split-window regression algorithm is used for GOES-16 LST EDR generation
GOES-16 LST EDR consists of three products: Full Disk (FD), CONUS, and Meso-scale (MESO1 and MESO2)
Users request
  EMC User’s request for verification of weather forecasting model output
  one of the Essential Climate Variables (ECVs) by the GCOS of the WMO
  General users for long-term global LST monitoring, agriculture monitoring, drought prediction, ecosystem monitoring, and climate studies, etc.
Notes: Current algorithm does not use the term of the emissivity difference between band 14 and 15. Our efforts have been focused on the enterprise algorithm for testing of this.

## Slide 5: Mission Requirement
Products | LST (Skin): CONUS | LST (Skin): Full Disk | LST (Skin): Mesoscale
Geographic Coverage | CONUS | Full Disk | Mesoscale
Horizontal Resolution | 2km | 10km | 2km
Mapping Accuracy | 1km | 5km | 1km
Measurement Range (K) | 213 – 330 | 213 – 330 | 213 – 330
Measurement Accuracy1 (K) | 2.5 | 2.5 | 2.5
Measurement Precision (K) | 2.3 | 2.3 | 2.3
Refresh Rate | 60 minutes | 60 minutes | 60 minutes
Vendor Allocated Ground latency | 3236 seconds | 806 seconds | 159 seconds
Extent Qualifier | Local Zenith Angle < 70 | Local Zenith Angle < 70 | Local Zenith Angle < 70
1 The measurement accuracy 2.5 K is conditional with 1) known emissivity, 2) known atmospheric correction, and 3) 80% channel correction; 5K otherwise. |  |  | 
Notes: Part of the requirement is outdated.
For historical reason, the Full Disk LST resolution is 10 km. This has a few drawbacks:
LST has large variability in space, such a coarse resolution is not enough for many studies;
This requires extra processing step of aggregation;
Aggregation algorithm is not available to AWG LST team, we can not reproduce the Full Disk product locally and therefore some issues can not be easily verified;
10 km is much larger than the footprint of in-situ stations (~ a few tens meters), leading to a large validation uncertainty.
All three products are hourly, which can not reflect the quick change of LST and fails to take advantage of the rapid scan by ABI, e.g., 15 min for FD, 5 min for CONUS, and 1 min for two MESOs for mode 3.

## Slide 6: LST processing flow (AER)
LST retrieved if
  good pixel availability
        input data not out of space
        input data not bad data
        input data not missing
  not over ocean
  clear or probably clear
    not probably cloudy
    not cloudy

## Slide 7: Beta Review: Time-Line/Context
19 Nov 2016 GOES-R Launch
29 Nov 2016 GEO orbit attained (became GOES-16)
03 Jan 2017 ABI aperture door open/1st light for visible/near-infrared channels
Mid Jan 2017: AWG established access to GS L2 products. Numerous LST related ADRs/WRs opened. LST L2 product validation begins.
24 May 2017 PS-PVR Beta
PLPT ID | Descriptive Title | % Complete | Results | AWG POC
ABI-FD_LST01 | verify that Mode 3 hourly FD products are within range | 100 | Complete | AWG
ABI-CONUS_LST02 | verify that Mode 3 hourly CONUS products are within range | 100 | Complete | AWG
ABI-MESO_LST03 | verify that Mode 3 hourly mesoscale products are within range | 100 | Complete | AWG
ABI-FD_LST04 | verify that Mode 4 hourly FD products are within range | 100 | Complete | AWG
ABI-CONUS_LST05 | verify that Mode 4 hourly CONUS products are within range | 100 | Complete | AWG
ABI-FD_LST06 | initial assessment of FD product accuracy and precision | 100 | Complete | AWG
ABI-CONUS_LST07 | initial assessment of CONUS product accuracy and precision | 100 | Complete | AWG
ABI-MESO_LST08 | initial assessment of mesoscale product accuracy and precision | 100 | Complete | AWG

## Slide 8: Risks to Reaching Provisional (Summary Status at PS-PVR Beta)
Risk | Description | Impact | Mitigation | Current Status
Significant underestimate at certain locations | Satellite retrieval is significantly lower compared to the in-situ at Desert Rock | Major | LST team is currently working on its possible cause and fixes. | The unit of TPW being used in LST retrieval is corrected, the underestimate at Desert Rock site improves.
outdated Emissivity used | Seebor emissivity used in LST retrieval might not be tuned to ABI sensor. | Major | LST AWG has developed the split-window channel emissivity for ABI sensor. | LST AWG developed the emissivity product for ABI sensor. Implementation in operational LST retrieval is not scheduled yet.
TPW data outage | GS update leads to unavailable TPW, which LST retrieval relies on | Unknown | LST team will monitor this issue. | Normal
LUT sensitivity | Retrieval threshold values will need to be tuned and updated | Minor | LST Team is working to tune the algorithm threshold values to improve the retrieval performance | New LUT is tested for Enterprise LST algorithm
FD LST aggregation impact | Pixel size of FD LST is 10 km and has large mismatch with the SURFRAD in-situ (~ a few tens meters) | Unknown | TBD | Validation results with in-situ observations is acceptable. Site characterization is being studied.
Navigation / Registration | Errors in sensor navigation/registration might degrade the LST data performance, though the band to band co-registration issue has been greatly reduced since L1b data beta maturity. | Unknown | LST team are keeping monitoring the issue. | No obvious navigation/registration issues have been found.
Notes: TPW is an import variable to determine which coefficient set is being used for specific pixel. The ground system incorrectly used TPW in mm instead of cm, which leads to significant bias in the LST product. The LST AWG team reported the issue on 6/23/2017 and it got fixed in OE since 1/25/2018 16:00 (UTC).
Emissivity used in LST retrieval is Seebor emissivity, which is not tuned up for real-time operational LST retrieval. The LST AWG team has developed its own daily emissivity product specific for ABI sensor. But a possible schedule of its implementation in the ground system is unknown.
The LST team used to identify horizontal shift of one or more pixels between Band 14 and 15 at some time stamps before May 2017 by visual inspection. It has not been observed in more recent data.
Retrieval threshold????

## Slide 9: Issues Needing Resolution for Provisional Maturity
Title | Description | Impact | Mitigation | Status
ADR198 | Incorrect radiance to BT conversion parameters | Incorrect parameters lead to miscalculated BT values and degrade the LST retrieval. | DO.05.00.00 | Installed
ADR216 | navigation/registration between band 14 and 15 | There is a relative shift of one or more pixels between Band 14 and 15 occasionally, which LST retrieval relies on. |  | Not found in recent data.
Geo-location | Geo-location file unavailable | Small difference between locally calculated and official data | Locally calculated before fix | Available
Solar and sensor angles | Solar and sensor angles unavailable | Small difference between locally calculated and official data | Locally calculated before fix | Available
ADR547 | Unit of TPW used in LST retrieval is incorrect | Coefficients for wet conditions are used for most pixels with dry conditions | PR.06.08 | Installed
Missing data | Missing lines in data | Visualization issue | DO.05 | Installed
ADR340 WR4511 | LST retrieval available under cloudy or probably cloudy conditions | At high sensor angle area (> 70), LST retrieval becomes available under cloudy or probably cloudy conditions. | PR.06.10 | Awaiting installation
Little Impact
Moderate Impact
Big Impact

## Slide 10: Product quality evaluation
GOES-16 Land Surface Temperature L2 Product Provisional PS-PVR

## Slide 11: Top Level Summary of Product Quality
The LST product quality improved
  Overall performance compared to in-situ observations is good
  Significant improvement of the underestimate at Desert Rock site with TPW issue fixed.
LST Product is ready for operational use and for use in comprehensive cal/val activities and product optimization.
Notes: The fix of TPW issue deceases the overall underestimate by satellite LST, especially at the Desert Rock site.

## Slide 12: Provisional PLPTs
Test ID | Test Title
ABI-FD_LST09 | FD product accuracy and precision assessment
ABI-CONUS_LST10 | CONUS product accuracy and precision assessment
ABI-MESO_LST11 | MESO product accuracy and precision assessment
AWG Land Surface Temperature Team will conduct these tests to further evaluate the L2 LST product quality.
Full test plans and procedures are given in the ABI LST Beta, Provisional, and Full Validation Readiness, Implementation, and Management Plan (RIMP v1.0; 416-R-RIMP-0331)

## Slide 13: Visual Inspection

## Slide 14
Full Disk LST
2018-02-20
Notes: FD LST looks normal. We used to observe lots of missing blocks and lines during beta PS-PVR.

## Slide 15
CONUS LST
2018-02-20
Notes: CONUS LST looks normal. We used to observe lots of missing blocks and lines during beta PS-PVR.

## Slide 16
Mesoscale LST: 2018-02-20
NESO1
NESO2
Notes: Hourly MESO LST output fails to reveal lots of details in LST.
For example, a case study has been carried out to study the outcome by Hurricane Maria. We can see signals from radiance (band 14 and 15) over land under clear or probably clear conditions due to its high output frequency but can not find any LST retrievals from the hourly LST product.

## Slide 17: LST, DQF, and PQI Inspection

## Slide 18: Quality Flag Inspection
Bit | Flag | Source | Effect
2-3 | Availability | SDR | 00=normal, 01=out of space, 10=bad data, 11=missing data
6-7 | Cloud Index | Cloud Mask | 00=clear, 01=probably clear, 10=probably cloudy, 11=cloudy
4-5 | Surface Type | Land/sea Mask | 00=land, 01=snow/ice, 10=in-land water, 11=sea
12-13 | LST Quality | LST | 00=normal, 01=cold surface (<250 K & >=213K), 10= out of range (not in 213-330K)
Bit | Flag | Source | Effect
1 | Availability | SDR | 0=normal, 1=out of space, bad data, missing data
2 | Cloud Index | Cloud Mask | 0=clear or probably clear, 1=probably cloudy, or cloudy
4 | Surface type | Land/sea mask | 0 = land, including inland water, 1= water
5 | LST Quality | LST | 0=normal, 1= out of range (not in 213-330K)
LST PQI
LST DQF
Notes: Not all input data for LST retrieval are available to the LST AWG.
The purpose of this inspection is to check if the LST values, DQF, and PQI are consistent with each other.

## Slide 19: Definition of Error Codes
101: DQF = 0 but PQI = 1
102: DQF = 0 but PQI = 2 should be 0
103: DQF = 0 but PQI = 3
104: DQF = 1 but PQI = 0 should be 1
111*: DQF = 1 and PQI = 1, 2, or 3 but LST retrieved should be no retrieval
201: DQF = 0 but PQI = 2
202: DQF = 0 but PQI = 3
203: DQF = 1 but PQI = 0
204: DQF = 1 but PQI = 1
211: DQF = 1 and PQI = 2 or 3 but LST retrieved
301*: DQF = 0 but PQI = 3 should be 0,1, or 2
302: DQF = 1 but PQI = 0
303: DQF = 1 but PQI = 1
304: DQF = 1 but PQI = 2
311: DQF = 1 and PQI = 3 but LST retrieved
401: DQF = 0 but PQI = 2 should be 0 or 1
402: DQF = 1 but PQI = 0
403: DQF = 1 but PQI = 1
404*: PQI = 3 Should be 0,1,or 2
411: 250.<=LST<=330. but PQI<>0
412: invalid LST but DQF(availability)=0 and DQF(surface type)=0 and DQF(cloud)=0 and PQI (quality)<>2
413: 213.<=LST<250. but PQI<>1
414: (LST<213. or LST>330.) but PQI<>2
Availability
Cloud Index
LST Quality
Surface Type
*NA to FD LST
Should be 0 or 1
Should be 2 or 3
Should be 3
Should be 2
Notes: Definition of error codes based on the metrics defined in previous slide.
Error 211: both DQF and PQI suggests the pixel is under cloudy or probably cloudy conditions, but LST retrieval is available

## Slide 20: Quality Flags
Products | Error Code |  |  |  | 
 | 101 | 102 | 103 | 104 | 111
FD |  |  |  |  | 
CONUS |  |  |  |  | 
MESO1 |  |  |  |  | 
MESO2 |  |  |  |  | 
Products | Error Code |  |  |  | 
 | 201 | 202 | 203 | 204 | 211
FD |  |  |  |  | 
CONUS |  |  |  |  | 
MESO1 |  |  |  |  | 
MESO2 |  |  |  |  | 
Products | Error Code |  |  |  | 
 | 301 | 302 | 303 | 304 | 311
FD |  |  |  |  | 
CONUS |  |  |  |  | 
MESO1 |  |  |  |  | 
MESO2 |  |  |  |  | 
Products | Error Code |  |  |  |  |  |  | 
 | 401 | 402 | 403 | 404 | 411 | 412 | 413 | 414
FD |  |  |  |  |  |  |  | 
CONUS |  |  |  |  |  |  |  | 
MESO1 |  |  |  |  |  |  |  | 
MESO2 |  |  |  |  |  |  |  | 

x

Passed
Correction in process
Not passed
Availability
Cloud Index
LST Quality
Surface Type
LST intermediate product is not available, the analysis is based on data from DE
Mode 4 IP is unavailable for analysis
QF Flag inspection for FD LST is based on un-aggregated 2-km LST, DQF, and PQI from DE
Notes: Big improvement compared to beta PS-PVR
In both FD and CONUS LSTs, valid retrievals are found under cloudy or probably cloudy conditions. It only happens in large view angle area (> 70°). A potential bug in GS has been identified and the corresponding ADR and WR have been created. The fix will be included in PR 06.10.
Similar issues have not been found in MESO LST, because MESO coverage is much smaller and usually will not reach that far.

## Slide 21: CONUS LST at Cloudy Pixels
Normal Retrieval
Cloudy Condition Over Land
Ocean
Retrieval Under Cloudy Condition
High Sensor Zenith Angle (>70º)

## Slide 22: FD LST at Cloud Conditions
Normal Retrieval
Cloudy Over Land
Valid Retrieval at Pixels with Mixed Cloud Conditions
LST Retrieval under Cloudy Condition (Sensor Angles > 70º)
Ocean
High Sensor Zenith Angle (>70º)
Notes: Yellow colors indicate retrievals with mixed cloud conditions (due to aggregation).

## Slide 23: LST metadata Inspection

## Slide 24: Product Metadata

x

Passed
explained
Not passed
Products | Min | Max | Mean | Std | Good | Retrieved | outlier
MESO1 |  |  |  |  |  |  | 
MESO2 |  |  |  |  |  |  | 
CONUS M3 |  |  |  |  |  |  | 
CONUS M4 |  |  |  |  |  |  | 
FD M3 |  |  |  |  |  |  | 
FD M4 |  |  |  |  |  |  | 
CONUS M4 LST is retrieved from subset FD M4 data, the calculation of product metadata in operational system is based on blocks which might consist of pixels out of CONUS.
Outlier in FD is inconsistent between the local calculation and OE output.
Notes: CONUS M4 metadata is based on blocks, some of which might consists of areas out of CONUS. This leads to the inconsistency between the metadata calculated locally and those included in the official product.
Aggregation procedure is not available to AWG LST team, the reason of inconsistent outlier calculation is unclear.

## Slide 25: DQF Metadata
* xy: x denotes the xth bit of DQF, and y is its value.
Analysis is based on DE data;
FD end product and intermediate product from DE are in different resolution, analysis is not applicable;
Mode 4 CONUS LST is retrieved from subset M4 data, the calculation of product metadata in operational system is based on blocks which might consist of pixels out of CONUS.
After drifting, the normalization factor used in OE/DE is incorrect.
Prod | 10* | 11 | 20 | 21 | 30 | 31 | 40 | 41 | 50 | 51 | Good
MESO1 |  |  |  |  |  |  |  |  |  |  | 
MESO2 |  |  |  |  |  |  |  |  |  |  | 
CONUS M3 |  |  |  |  |  |  |  |  |  |  | 
CONUS M4 |  |  |  |  |  |  |  |  |  |  | 
Prod | 10* | 11 | 20 | 21 | 30 | 31 | 40 | 41 | 50 | 51 | Good
MESO1 |  |  |  |  |  |  |  |  |  |  | 
MESO2 |  |  |  |  |  |  |  |  |  |  | 
CONUS M3 |  |  |  |  |  |  |  |  |  |  | 
CONUS M4 |  |  |  |  |  |  |  |  |  |  | 
GOES-Test
GOES-East

x

Passed
explained
Not passed
Notes: GOES-Test: before the satellite drift (89.5°W)
GOES-East: after the satellite drift (75.2°W projected to 75°W)
The change of satellite location change its view and coverage of CONUS area.
Incorrect normalization factor is common among CONUS products.
Digit 1: Availability; 2: Cloud Index: 3: View Angle ; 4: Surface Type; 5: LST Quality

## Slide 26: Product quality assessment with SURFRAD in-situ observations

## Slide 27: Definitions of Metrics for Quantitative Comparisons
Passed: Accuracy and Precision meet or slightly exceed requirements. Potential contributors for deviations are identified.
Partial-Passed: Accuracy/Precision deviates significantly from requirements, but potential contributors for deviations are identified.
Failed: Accuracy/Precision deviates significantly from requirements and source of poor performance is unknown, or source known and correction requires new algorithm.

## Slide 28: In-situ ground observation data
SURFRAD Sites
  Surface Radiation Budget Network (SURFRAD) – 7 operational sites in CONUS
    Radiometer measuring broadband radiation every minute
    Available within a day or two of observation
    Instrument calibrated annually and well maintained
  We need data outside US, in Central and South America
Notes: 28
High-quality in-situ validation site for LST is very limited.
More sites needed in Central and South America.
28

## Slide 29: TPW issue in LST Retrieval
Unit of TPW used in LST retrieval is incorrect (mm instead of cm), leading to incorrect coefficient selected for retrieval TPW issue got fixed since 16:00 Jan. 25, 2018
Left two figures: validation results from operational products before TPW issue was fixed
Right two figures: validation results based on locally calculated LST with TPW issue corrected
The underestimate at Boulder and Desert Rock sites significantly improves with TPW issue fixed in Local-calculated LST.
CONUS LST Validation Results before TPW issue was fixed
TPW incorrect (official)
TPW corrected (local)

## Slide 30: CONUS LST Validation Results – since TPW issue was fixed
Site | Operational Product |  |  | Local calculation |  | 
 | Number | Accuracy (K) | Precision (K) | Number | Accuracy (K) | Precision (K)
Bondville_IL | 24 | 0.32 | 2.00 | 24 | 0.32 | 2.00
Boulder_CO | 16 | -1.05 | 1.59 | 16 | -1.05 | 1.59
Desert_Rock_NV | 25 | -3.11 | 1.21 | 25 | -3.11 | 1.21
Fort_Peck_MT | 29 | -0.11 | 0.56 | 29 | -0.11 | 0.56
Goodwin_Creek_MS | 45 | -1.42 | 1.70 | 45 | -1.42 | 1.70
Penn_State_PA | 10 | -0.92 | 1.20 | 10 | -0.92 | 1.20
Sioux_Falls | 27 | -2.65 | 1.04 | 27 | -2.65 | 1.04
Time series after TPW issue got fixed is too short to yield statistically significant analysis results
LST AWG has reproduced the operational product in local calculation environment using exactly the same input data
The following validation analysis will be based on locally calculated LST by AWG

## Slide 31: Reference Algorithm
The enterprise LST retrieval algorithm was used as a reference algorithm to compare with the baseline LST
Selected among 22 different algorithms
Accepted as the LST retrieval algorithm candidate for both GOES-R and JPSS missions.
Different from the baseline algorithm
  Emissivity difference term is used
  Instead of a angle-correction term, the retrieval is stratified by sensor zenith angle
Notes: Most of the team’s efforts have been focused on the tuning and update of the enterprise algorithm. However, a possible implementation schedule is unknown yet.

## Slide 32: Validation Procedures
Direct comparison with SURFRAD in-situ measurements
Validate Data: 20170601 - Current
Cloud screening
  Intermediate Product unavailable for significant amount of validation period, i.e. four levels cloud information missing
  Based on 3x3 two-level cloud from DQF
Additional cloud filtering
  In-situ downwelling radiation time series
  Satellite 3x3 Brightness Temperature at ~11 µm (band 14)
Notes: 20170601: when clear sky mask product is declared provisional

## Slide 33: CONUS LST Validation
Site | Number | Local calculation |  | Enterprise Algorithm | 
 |  | Accuracy (K) | Precision (K) | Accuracy (K) | Precision (K)
Bondville_IL | 1442 | 0.33 | 1.90 | 0. 45 | 1.85
Boulder_CO | 1254 | -1.13 | 1.43 | -1.18 | 1.45
Desert_Rock_NV | 1048 | -3.42 | 1.28 | -3.28 | 1.25
Fort_Peck_MT | 1264 | -0.63 | 1.46 | -0.99 | 1.41
Goodwin_Creek_MS | 1802 | 1.06 | 2.40 | 1.39 | 2.30
Penn_State_PA | 928 | 0.57 | 2.14 | 0.54 | 2.05
Sioux_Falls | 1476 | -0.43 | 1.92 | -0.54 | 1.87
All Sites | 9214 | -0.38 | 1.87 | -0.36 | 1.81
Notes: Validation results at most sites are good.
Significant underestimate at Desert Rock can be observed even though it is improved by fixing the TPW issue.
Precision requirement is marginally met at Goodwin Creek site.
Overall statistics suggests the mission requirement has been met.
In general, the enterprise algorithm is superior to baseline algorithm.
Even though TPW issue was not fixed during most of the time series of official LST product, its overall statistics meet the mission requirement (Backup slides)

## Slide 34: CONUS LST Validation
Notes: Baseline algorithm

## Slide 35: CONUS LST Validation

## Slide 36: Full Disk LST Validation
Site | Before TPW fixed |  |  | After TPW fixed |  | 
 | Number | Accuracy (K) | Precision (K) | Number | Accuracy (K) | Precision (K)
Bondville_IL | 620 | -0.69 | 1.97 | 38 | -0.02 | 1.37
Boulder_CO | 510 | -2.03 | 1.93 | 5 | -0.43 | 1.91
Desert_Rock_NV | 300 | -5.71 | 1.67 | 0 | NA | NA
Fort_Peck_MT | 403 | -1.44 | 1.95 | 5 | 0.70 | 1.42
Goodwin_Creek_MS | 643 | 3.59 | 2.08 | 9 | 0.21 | 0.76
Penn_State_PA | 329 | 1.59 | 2.41 | 19 | 0.80 | 0.89
Sioux_Falls | 633 | -0.08 | 1.48 | 12 | -2.08 | 1.30
All Sites | 3438 | -0.28 | 1.93 | 88 | -0.08 | 1.22
Notes: Since aggregation procedure is not available to LST AWG team, FD LST local calculation similar to CONUS LST can not be done.
Serious underestimate at Desert Rock site and overestimate at Goodwin Creek site before TPW issue got fixed.
Statistics after TPW issue was fixed are good, however, the time series is too short for statistically significant conclusions.

## Slide 37: MESO
Site | Number | Local calculation |  | Enterprise Algorithm | 
 |  | Accuracy (K) | Precision (K) | Accuracy (K) | Precision (K)
Bondville_IL | 796 | 0.27 | 1.82 | 0.55 | 1.75
Boulder_CO | 68 | -1.14 | 2.11 | -1.22 | 2.08
Desert_Rock_NV | 104 | -3.25 | 1.61 | -3.04 | 1.57
Fort_Peck_MT | 28 | -0.95 | 1.81 | -1.16 | 1.60
Goodwin_Creek_MS | 817 | 1.16 | 2.62 | 1.50 | 2.50
Penn_State_PA | 485 | 0.81 | 2.63 | 0.80 | 2.58
Sioux_Falls | 149 | -0.52 | 2.21 | -0.54 | 2.08
All Sites | 2447 | 0.43 | 2.30 | 0.63 | 2.22
Notes: Overall statistics suggest that the requirement has been met

## Slide 38: GOES-16 LST vs. SURFRAD LST
Site | Specifications Met Products? |  |  |  |  | 
Domain | CONUS |  | Full Disk |  | MESO1 | 
Site | Accuracy | Precision | Accuracy | Precision | Accuracy | Precision
Bondville_IL | √ | √ | √ | √ | √ | √
Boulder_CO | √ | √ | √ | √ | √ | √
Desert_Rock_NV | × | √ | × | √ | × | √
Fort_Peck_MT | √ | √ | √ | √ | √ | √
Goodwin_Creek_MS | √ | × | × | √ | √ | ×
Penn_State_PA | √ | √ | √ | × | √ | ×
Sioux_Falls_SD | √ | √ | √ | √ | √ | √
All Sites | √ | √ | √ | √ | √ | √
Period : June 1, 2017 – February 18, 2018

## Slide 39: Summary
The overall validation results indicate satisfactory performance for baseline product
Validation results vary by different sites.
Satellite LST is significantly lower than its in-situ counterpart at Desert Rock site
Quality if cloud identification is key to LST performance and validation
Site homogeneity is crucial in LST validation
Notes: Performance of enterprise algorithm is better than baseline.

## Slide 40: Case 1
Desert Rock Site

## Slide 41: Desert Rock Validation Results --Multiple satellites
Four years LST time series from AQUA, TERRA, and SNPP are compared to Desert Rock LST as a comparison
ABI LST underestimate at Desert Rock site is comparable to AQUA and TERRA LST
SNPP VIIRS LST performs much better with an underestimate as low as 0.31 k
              Surface Type dependent algorithm, coefficient can be easily fine-tuned for any specific surface type

## Slide 42: Desert Rock Site Elevation
30 km
30 km
Surface elevation of a 30 km x 30 km box centered at Desert Rock site is shown (right figure)
Surface topography is complicated, ranging from 731 m (South West corner) to 2228 m (South)
Though surface emission characteristic is quite homogeneous, surface temperature is not due to high elevation variability
GOES-16 pixel is larger than that of LEO, leading to larger uncertainty in validation.
Desert Rock Station
CONUS Pixel Center
FD Pixel Center

## Slide 43: Case 2
Goodwin Creek Site

## Slide 44
FD Pixel Center
CONUS Pixel Center
In-situ Site
10 KM
10KM
Validation based on direct comparison with in-situ observation: pixel to point
Site representativeness of the satellite pixel is key: good homogeneity required
The complicated surface type shown on the right leads to high uncertainty when comparing the point temperature to pixel temperature
Full Disk LST has 10 km resolution at nadir, a homogeneous site in such a large area is not available in CONUS.

## Slide 45: Case 3
Cloud Detection

## Slide 46: Quality Control
a
b
c
d
e
Notes: Statistics in each figure shown all matchups in both black and red colors. Red colors are those which can not meet a certain qc procedure and will be filtered out in the next figure.
Figures a, b, and c are common additional cloud filtering procedures used in LST validation by AWG LST team.
Figure d shows QC procedure specific to Bondville site due to its own characteristics. Red means the daytime matchup between 5/31/2017 and 6/15/2017. The improvement by filtering out the red matchup is dramatic (see results in figure e)
Figure e: There are still outliers left after the previous QC procedures.

## Slide 47: Site Homogeneity
2 km
2 km
CONUS Pixel Center
In-situ Site
Notes: Right figure is typical during late spring/early summer around this site. The view by satellite is significantly different from the view by the in-situ tower (grassland).
Similar overestimate are also found in SNPP VIIRS LST during the same season.

## Slide 48: Potential Cloud Contamination? 2017-10-08 21:47
LST_Satellite: No retrieval Due to Cloud
LST_Ground: 294.853
Matchup Satellite Pixel

## Slide 49: Potential Cloud Contamination? 2017-10-08 22:47
LST_Satellite: 273.800
LST_Ground: 293.617
Matchup Satellite Pixel
Notes: The bondville site is located near the cloud edge area. 22:47:21.8 shows clear, one hour before and later are cloudy.
The lack of LST IP does not allow us to do more detailed analysis based on four-level cloud mask.

## Slide 50: Potential Cloud Contamination? 2017-10-08 23:47
LST_Satellite: No retrieval Due to Cloud
LST_Ground: 291.507
Matchup Satellite Pixel

## Slide 51: Comparison with SNPP VIIRS LST

## Slide 52: Data
LST products and associated data:
  EDR: LST;
  SDR: BT11, BT12;
  Ancillary: VIIRS Surface type EDR, viewing/solar geometry data, GTOPO Global DEM data;
24 days data are used in the comparison (one day per week, 2017.05 ~ 2017.10);
Final count of match-up data pairs:
GOES16 ABI Grid
LEO pixel
LEO pixel center
Included for ABI grid
Not included for ABI grid
Aggregation scheme

## Slide 53: Example of Comparison -- ABI LST v.s. SNPP VIIRS
Notes: ABI LST agrees well with aggregated VIIRS LST

## Slide 54: Comparison Summary
Median (50% Quantile)
Mean
25% Quantile
75% Quantile
Notes: The box plots show the overall summary for match-up data pairs between GEO and LEO products over CONUS (for LST, BT11, BT12, BT difference term (i.e., BT11-BT12), and Viewing angle.
The meaning of the box plot is listed on the right bottom. The range of the box plot indicates the range of middle 50% data pairs.
All items (except) LST are variables for LST retrieval algorithm.
ABI LST shows highest agreement with the MYD11 (Aqua MODIS) LST products comparing to other two LEO LST products (MOD11 and VIIRS LSTs).

## Slide 55: Dependency Analysis
Correlation matrix show BT differences are the dominant factor for LST differences between LEO and GEO prodcuts.
Notes: These plots try to demonstrate which factors strongly relates with the LST differences between GOES-16 ABI and polar orbiting satellite products (MOD11/MYD11/VIIRS).
The factors include (from left to right, from bottom to left):
Delta(LST) : LST difference (ABI minus polar orbiting)
Delta(BT11) : BT11 difference (ABI minus polar orbiting)
Delta(BT12) : BT12 difference (ABI minus polar orbiting)
Delta(BT11-BT12): (BT11-BT12) difference (ABI minus polar orbiting)
Theta(ABI) : ABI Sensor zenith angle
TPW(ABI) : ABI sensor zenith angle
Delta(theta) : sensor zenith angle difference (ABI minus polar orbiting)
E(ABI) : Emissivity value used for ABI LST retrieval (historical value from Wisconsin dataset)
u : solar zenith angle
Each grid represents the correlation coefficient between two variables. For example, the first colored grid (top-left) is the correlation coefficient between LST difference and BT11 difference. The number in each grid is the correlation coefficient for that variables pair.
FIRST ROW of the matrix is the focus of this plot, which demonstrate the major factors relate to the LST difference, which are BT11 difference, BT12 difference, (BT11-BT12) difference, TPW and emissivity.
Other grids also show potential covariability btween different factors, such as the TPW are highly correlated with BT differences, which might leads to high correlation in first row.

## Slide 56: Dependency Analysis
IGBP Surface type: LEO/GEO LST difference has larger variations over sparse vegetated surface types, such as shrubland/savannahs/grasslands (6-10), barren (16) and evergreen needle-leaf forests (1, which is usually in high latitude/viewing angle region).
Notes: Time period:
2017.05 ~ 2017.10 (one day from each week within this time period, 25 days in total)
Temporal difference:
less than 7.5 minutes
Data pair screening:
1. ABI cloud mask equals to “0” (clear)
2. clear (“0”) VIIRS/MODIS pixel ratio within the ABI grid is higher than 75%.
All the differences are the ABI value minus MODIS/VIIRS value.
The center black line in the box plot indicate the median value of all data pairs, while the lower end of the box is the 25% quantile of the data pairs, and the upper end of the box is the 75% quantile of the data pairs. This means 50% of the data pairs are in the range of the box.
The IGBP surface type is aggregated from VIIRS Surface type EDR product. The majority surface type within each ABI grid is used as the grid surface type.

## Slide 57: Dependency Analysis
Mean elevation: LEO/GEO LST difference show dependence on the mean elevation. For low elevation region. This dependence is suspected to be a combined result of terrain and view zenith angle.
Notes: Time period:
2017.05 ~ 2017.10 (one day from each week within this time period, 25 days in total)
Temporal difference:
less than 7.5 minutes
Data pair screening:
1. ABI cloud mask equals to “0” (clear)
2. clear (“0”) VIIRS/MODIS pixel ratio within the ABI grid is higher than 75%.
All the differences are the ABI value minus MODIS/VIIRS value.
The center black line in the box plot indicate the median value of all data pairs, while the lower end of the box is the 25% quantile of the data pairs, and the upper end of the box is the 75% quantile of the data pairs. This means 50% of the data pairs are in the range of the box.
The elevation is aggregated from GTOPO30 Global 30 Arc-Second Elevation data by averaging.

## Slide 58: Dependency Analysis
Viewing angle: LEO/GEO LST difference show strong dependence on satellite viewing angle differences. Larger ABI viewing angle translate to negative LST difference between ABI and LEO LST products. This dependency is much stronger for daytime observations than nighttime data.
Notes: Time period:
2017.05 ~ 2017.10 (one day from each week within this time period, 25 days in total)
Temporal difference:
less than 7.5 minutes
Data pair screening:
1. ABI cloud mask equals to “0” (clear)
2. clear (“0”) VIIRS/MODIS pixel ratio within the ABI grid is higher than 75%.
All the differences are the ABI value minus MODIS/VIIRS value.
The center black line in the box plot indicate the median value of all data pairs, while the lower end of the box is the 25% quantile of the data pairs, and the upper end of the box is the 75% quantile of the data pairs. This means 50% of the data pairs are in the range of the box.

## Slide 59: Dependency Analysis
For different combination of GEO (x) and LEO (y) viewing angle combination, the dependence of LST differences show a strong dipole pattern (except IDPS VIIRS LST products). Mean differences are largest when viewing angles differences are the largest (top left and bottom right corner of each plots).
Notes: These plots show the distribution of LST differences along different combinations of ABI STZ (x-axis) and polar orbiting sensor STZ (y-axis).
The cross comparison is focus on CONUS (date range from May to October, one-day per week, with total 24-day data). Total number of data pairs are listed in the data density plot.
The grey-filled grids are grids with no data pairs available. The dotted black line indicates the 1:1 line, which are grids have same satellite zenith angles from both ABI and polar orbiting sensors.
Since this is based on the CONUS ABI products, so no nadir data from ABI are available. Also, majority of data pairs are pixels with STZ larger than 30 degrees from ABI.

## Slide 60: Dependency Analysis
For different combination of GEO (x) and LEO (y) viewing angle combination, the variation of LST difference (or standard deviation) between LEO and GEO products show increasing trend when the ABI viewing angle increases.
Notes: These plots show the distribution of LST differences along different combinations of ABI STZ (x-axis) and polar orbiting sensor STZ (y-axis).
The cross comparison is focus on CONUS (date range from May to October, one-day per week, with total 24-day data). Total number of data pairs are listed in the data density plot.
The grey-filled grids are grids with no data pairs available. The dotted black line indicates the 1:1 line, which are grids have same satellite zenith angles from both ABI and polar orbiting sensors.
Since this is based on the CONUS ABI products, so no nadir data from ABI are available. Also, majority of data pairs are pixels with STZ larger than 30 degrees from ABI.

## Slide 61: Provisional Maturity Assessment
GOES-16 Derived Motion Winds L2 Product Provisional PS-PVR

## Slide 62: Provisional Validation
Preparation Activities | Assessment
Validation activities are ongoing and the general research community is now encouraged to participate. | Validation activities are ongoing. The user community has been participating.
Severe algorithm anomalies are identified and under analysis. Solutions to anomalies are in development and testing. | Operational and algorithm anomalies have been identified. Critical ones have been resolved; only one LST ADR remains to be implemented.
Incremental product improvements may still be occurring. | Incremental product improvements are expected.

## Slide 63: Provisional Validation
End State | Assessment
Product performance has been demonstrated through analysis of a small number of independent measurements obtained from select locations, periods, and associated ground truth or field campaign efforts. | This has been demonstrated.
Product analysis is sufficient to communicate product performance to users relative to expectations (Performance Baseline). | This has been communicated in PS-PVR.
Documentation of product performance exists that includes recommended remediation strategies for all anomalies and weaknesses. Any algorithm changes associated with severe anomalies have been documented, implemented, tested, and shared with the user community. | These are documented in this slide and will be documented in a separate report.
Testing has been fully documented. | Testing will be documented in a PLPT Report.
Product is ready for operational use and for use in comprehensive cal/val activities and product optimization. | Agree

## Slide 64: Recommendation
AWG LST Team believes that the GOES-16 LST L2 product has reached the Provisional Maturity as defined by the GOES-R Program

## Slide 65: Path to full Validation Maturity
GOES-16 Derived Motion Winds L2 Product Provisional PS-PVR

## Slide 66: Path to Full Validation Maturity
We expect to carry out the same activities for full validation maturity
  More than one year of subset data centered at SURFRAD stations have been accumulated including L1, L2, and IPs.
  The collection of subset data will continue throughout year 2018. This is crucial, the current LST time series since TPW issue fix is too short to reach statistically significant conclusions.
  Case studies will be carried out.
  We will fine tune algorithm coefficients and the related threshold values for better retrieval performance.
  Comparison with polar orbit satellite LST will continue
Currently outstanding issues, unless fixed by handover, may prevent declaration of Operational Maturity
  LST retrieval available under cloudy or probably cloud conditions at large sensor angle area (> 70°)

## Slide 67: Issues
The fix of TPW issue significantly decreases the significant LST underestimate at one SURFRAD site, however, it is still higher than expected
Emissivity used in operational LST retrieval is from historical Seebor emissivity product, this might degrade the LST retrieval performance
Access to LST intermediate product is needed for detailed validation with respect to four-level cloud conditions.
Full Disk LST resolution of 10 km is significantly larger than the SURFRAD in-situ footprint (~ a few tens meters).
LST retrieval is available under cloudy or probably cloudy conditions at large sensor zenith angles (> 70°)
  PR (ADR 340; WR4511) is ready.

## Slide 68: Full Validation PLPTs
PLPT ID | Descriptive Title
ABI-FD_LST12 | FD product accuracy and precision assessment
ABI-CONUS_LST13 | CONUS product accuracy and precision assessment
ABI-MESO_LST14 | MESO product accuracy and precision assessment
AWG LST Team will conduct these tests to further evaluate the L2 LST product quality.
Full test plans and procedures are given in the LST Readiness, Implementation, and Management Plan (RIMP v1.0; 416-R-RIMP-0331)

## Slide 69: Path to Full Validation – Risks
Risk Name | Description | Impact | Mitigation and Schedule
Operation Stability | IF corrections for known anomalies cannot be implemented timely | THEN the operation will not reach steady state for evaluation | Raise awareness Work with Ground

## Slide 70: Summary & Recommendations
GOES-16 Derived Motion Winds L2 Product Provisional PS-PVR

## Slide 71: Summary
Overall, all three LST products meet the mission requirement of accuracy and precision.
  Validation results vary at different ground stations.
  Mission requirement are not met at some stations.
The LST product performance is improved since TPW issue was fixed (01/25/2018).
  Time series after the fix is too short to yield statistically significant results.
  LST product is more useable starting ~ 16Z on 01/25/2018
  AWG LST team has locally corrected the TPW issue and the results are consistent with the baseline product since the fix.

## Slide 72: Recommendation
AWG Land Surface Temperature Team believes that the GOES-16 LST L2 product has reached the Provisional Maturity as defined by the GOES-R Program

## Slide 73: Backup
GOES-16 DMW L2 Product Provisional PS-PVR

## Slide 74: GOES-16 LST (CONUS Satellite)
Notes: This plot shows validation results of the official CONUS LST product (TPW issue not fixed until 1/25/2018 16:00 UTC)
The overall statistics suggest it meet the mission requirement.
Underestimate at Desert Rock is near 5K, much more significant than the locally calculated baseline LST (TPW issue fixed)

## Slide 75: Elevation Map
Aggregated (average) elevation for ABI grids;
Data source:
  Global 30 Arc-Second Elevation data (GTOPO30, nearly 1km resolution)

## Slide 76: Surface Type Map
Aggregated IGBP surface types;
Data source: S-NPP surface type EDR.