## Slide 1: GOES-16 ABI L2+ LAP Products Provisional PS-PVR
Timothy J. Schmit
Chair, GOES-R series AWG LAP team
NOAA/NESDIS/STAR
22 February 2018
GOES-R AWG LAP team: Jun Li, Yong-Keun Lee,
Richard Dworak, Zhenglong Li

## Slide 2: Agenda
Review of Beta Maturity
Product Quality Evaluation
- PLPT Tests and Results
Provisional Validation Product Maturity Assessment
Path to Full Maturity
Summary and Recommendations

## Slide 3: REVIEW OF BETA MATURITY
GOES-16 ABI L2 LAP Product Provisional PS-PVR

## Slide 4: Products Overview
The GOES-16 ABI L2 LAP algorithm includes regression and physical retrieval based on the infrared spectral bands. The algorithm is applied to 5x5 ABI pixels (~10 km) for generating LAP products over clear sky. The LAP products include LVT, LVM, TPW, and DSI.
Band Number | Wavelength (µm) | Purpose
8 | 6.19 | High-level atmospheric water vapor, winds, rainfall
9 | 6.93 | Mid-level atmospheric water vapor, winds, rainfall
10 | 7.34 | Lower-level atmospheric water vapor, winds, and SO2
12 | 9.61* | Total ozone
13 | 10.33 | Surface and cloud
14 | 11.20 | Imagery, SST, clouds, rainfall
15 | 12.30 | Total water, ash, SST
16 | 13.30 | Air temperature, cloud heights and amounts
Notes: * Only used in the regression step.

## Slide 5: Review: Time-Line/Context
19 Nov 2016 GOES-R Launch
29 Nov 2016 GEO orbit attained (became GOES-16)
03 Jan 2017 ABI aperture door open/1st light for visible/near-infrared channels
Apr 2017: ABI L2 LAP baseline products validation begins.
16 May 2017 LAP PS-PVR Beta
30 Nov - 13 Dec 2017 Spacecraft Drift to East Slot
18 Dec 2017 Imagery operational

## Slide 6: Beta PLPTs Review
PLPT ID | Descriptive Title | % Complete | Results | AWG POC
ABI-FD_TPW01 | Verify Product is generated every hour for FD for M3 | 100 | Complete* | PRO
ABI-CONUS_TPW02 | Verify Product is generated every 30 min for CONUS for M3 | 100 | Complete* | PRO
ABI-MESO_TPW03 | Verify Product is generated every 5 min for Meso for M3 | 100 | Complete* | PRO
ABI-FD_TPW04 | Verify Product is generated every hour for FD for M4 | 100 | Complete* | PRO
ABI-CONUS_TPW05 | Verify Product is generated every 30 min for CONUS for M4 | 100 | Complete* | PRO
ABI-FD_TPW06 | Quantitative analysis of M3 FD TPW | 100 | Complete | AWG
ABI-CONUS_TPW07 | Quantitative analysis of M3 CONUS TPW | 100 | Complete | AWG
ABI-MESO_TPW08 | Quantitative analysis of M3 Meso TPW | 100 | Complete | AWG
Notes: PRO is responsible for 01 – 05.

## Slide 7: Beta PLPTs Review
PLPT ID | Descriptive Title | % Complete | Results | AWG POC
ABI-FD_LVT01 | Verify Product is generated every hour for FD for M3 | 100 | Complete* | PRO
ABI-CONUS_LVT02 | Verify Product is generated every 30 min for CONUS for M3 | 100 | Complete* | PRO
ABI-MESO_LVT03 | Verify Product is generated every 5 min for Meso for M3 | 100 | Complete* | PRO
ABI-FD_LVT04 | Verify Product is generated every hour for FD for M4 | 100 | Complete* | PRO
ABI-CONUS_LVT05 | Verify Product is generated every 30 min for CONUS for M4 | 100 | Complete* | PRO
ABI-FD_LVT06 | Quantitative analysis of M3 FD LVT | 100 | Complete | AWG
ABI-CONUS_LVT07 | Quantitative analysis of M3 CONUS LVT | 100 | Complete | AWG
ABI-MESO_LVT08 | Quantitative analysis of M3 Meso LVT | 100 | Complete | AWG
Notes: PRO is responsible for 01 – 05.

## Slide 8: Beta PLPTs Review
PLPT ID | Descriptive Title | % Complete | Results | AWG POC
ABI-FD_LVM01 | Verify Product is generated every hour for FD for M3 | 100 | Complete* | PRO
ABI-CONUS_LVM02 | Verify Product is generated every 30 min for CONUS for M3 | 100 | Complete* | PRO
ABI-MESO_LVM03 | Verify Product is generated every 5 min for Meso for M3 | 100 | Complete* | PRO
ABI-FD_LVM04 | Verify Product is generated every hour for FD for M4 | 100 | Complete* | PRO
ABI-CONUS_LVM05 | Verify Product is generated every 30 min for CONUS for M4 | 100 | Complete* | PRO
ABI-FD_LVM06 | Quantitative analysis of M3 FD LVM | 100 | Complete | AWG
ABI-CONUS_LVM07 | Quantitative analysis of M3 CONUS LVM | 100 | Complete | AWG
ABI-MESO_LVM08 | Quantitative analysis of M3 Meso LVM | 100 | Complete | AWG
Notes: PRO is responsible for 01 – 05.

## Slide 9: Beta PLPTs Review
PLPT ID | Descriptive Title | % Complete | Results | AWG POC
ABI-FD_DSI01 | Verify Product is generated every hour for FD for M3 | 100 | Complete* | PRO
ABI-CONUS_DSI02 | Verify Product is generated every 30 min for CONUS for M3 | 100 | Complete* | PRO
ABI-MESO_DSI03 | Verify Product is generated every 5 min for Meso for M3 | 100 | Complete* | PRO
ABI-FD_DSI04 | Verify Product is generated every hour for FD for M4 | 100 | Complete* | PRO
ABI-CONUS_DSI05 | Verify Product is generated every 30 min for CONUS for M4 | 100 | Complete* | PRO
ABI-FD_DSI06 | Quantitative analysis of M3 FD DSI | 100 | Complete | AWG
ABI-CONUS_DSI07 | Quantitative analysis of M3 CONUS DSI | 100 | Complete | AWG
ABI-MESO_DSI08 | Quantitative analysis of M3 Meso DSI | 100 | Complete | AWG
Notes: PRO is responsible for 01 – 05.

## Slide 10: Risks to Reaching Provisional
Risk Name | Description | Impact | Mitigation and Schedule
Missing values over randomly distributed areas | Frequently, there are missing values over randomly distributed boxed areas. | Minor | The filling values indicate no value regions. This is a result of using the terrestrial GRB at NSOF. Will be moving to RF GRB by Handover which will resolve this issue.
The migration of the sun affecting the LAP products | The ABI LAP products are affected by sun-rise and sun-set. | Minor | Cloud mask may have influences on the ABI LAP products.
Wet bias of the relative humidity in upper troposphere (100 - 300 hPa) | The relative humidity in upper troposphere (100-300 hPa) shows large wetter bias than the spec. | Minor | Radiosonde has dry bias in observing the relative humidity in the upper troposphere. So the comparison with ECMWF analysis data will be included for further tests.
Slightly large discrepancy of several DSI | Several DSI show slightly larger discrepancy than the spec. | Minor | If the atmospheric conditions are unstable, the statistics results are closer to the requirements.
Little Impact
Moderate Impact
Big Impact

## Slide 11: Upstream Algorithm Issues
Upstream Issue | Description | Impact | Algorithm Implications
ABI L1b - INR | Issues remain with ABI L1b INR issues associated with navigation and co-registration issues |  | 
ABI L1b – Stripping and Calibration | Image stripping is present in some imagery data. Calibration is still being evaluated on the system and seems to vary over time |  | 
ABI L2 Cloud Mask | Soundings need a high-quality upstream cloud mask |  | 
ABI L1b - GRB | Missing blocks of data | Major | Algorithm will not produce data in regions of missing blocks
Little Impact
Moderate Impact
Big Impact

## Slide 12: PRODUCT QUALITY EVALUATION
GOES-16 ABI L2 LAP Product Provisional PS-PVR

## Slide 13: Recommendations from Beta Review Team
Include ECMWF and GFS analysis as references (completed);
Include GOES-R field campaign data as reference (completed);
Include ABI Legacy Atmospheric Profile (LAP) spec along with validation results (completed);
Identify and understand the outliers in TPW comparisons with Suomi-Net GPS data (completed).

## Slide 14: Provisional PLPTs Under Review
PLPT ID | Descriptive Title | % Complete | Results | AWG POC
ABI-FD_TPW09 | Quantitative analysis of M3 FD TPW | 100 | Complete | AWG
ABI-CONUS_TPW10 | Quantitative analysis of M3 CONUS TPW | 100 | Complete | AWG
ABI-MESO_TPW11 | Quantitative analysis of M3 Meso TPW | 100 | Complete | AWG
TPW: Total Precipitable Water

## Slide 15: Provisional PLPTs Under Review
PLPT ID | Descriptive Title | % Complete | Results | AWG POC
ABI-FD_LVT09 | Quantitative analysis of M3 FD LVT | 100 | Complete | AWG
ABI-CONUS_LVT10 | Quantitative analysis of M3 CONUS LVT | 100 | Complete | AWG
ABI-MESO_LVT11 | Quantitative analysis of M3 Meso LVT | 100 | Complete | AWG
LVT: Legacy Vertical Temperature profile

## Slide 16: Provisional PLPTs Under Review
PLPT ID | Descriptive Title | % Complete | Results | AWG POC
ABI-FD_LVM09 | Quantitative analysis of M3 FD LVM | 100 | Complete | AWG
ABI-CONUS_LVM10 | Quantitative analysis of M3 CONUS LVM | 100 | Complete | AWG
ABI-MESO_LVM11 | Quantitative analysis of M3 Meso LVM | 100 | Complete | AWG
LVM: Legacy Vertical Moisture profile

## Slide 17: Provisional PLPTs Under Review
PLPT ID | Descriptive Title | % Complete | Results | AWG POC
ABI-FD_DSI09 | Quantitative analysis of M3 FD DSI | 100 | Complete | AWG
ABI-CONUS_DSI10 | Quantitative analysis of M3 CONUS DSI | 100 | Complete | AWG
ABI-MESO_DSI11 | Quantitative analysis of M3 Meso DSI | 100 | Complete | AWG
DSI: Derived Stability Indices

## Slide 18: PLPT Tests for each Domain
Analysis Method | FD | CONUS | MESO
Visual Inspection |  |  | 
Comparison to reference data (RAOB, GPS, AMSR2, ECMWF, GDAS, AERI) |  |  | 
Our 3 PLPTs dealing with analysis are comprised of the same 2 methods.
Each contains the applications of these methods on the FD, CONUS and MESO domains.
The applications of each method to each domain is summarized below.
Some methods were redundant or not possible for some domains.
Note that ECMWF, GDAS, AERI data are new in the LAP provisional validation.
18

## Slide 19: GOES-16 Data Used in this Review
April 2017-January 2018: All FD, CONUS, Meso1, and Meso2 LAP with RAOB, Suomi-Net GPS TPW, and AMSR2 TPW matchups within +/- 30 min, 20 km (RAOB and GPS) and 10 km (AMSR2), and 20 km (ECMWF and GDAS);
Day 182 (July 1, 2017), 2000 UTC: Visual images of all domains for each variable;
Day 182, 0800, 0900 UTC: To show the migration of the sun affecting TPW;
Day 182, 0000, 0230 UTC: To show missing data over randomly distributed boxed areas in TPW.
19

## Slide 20: Definitions of Metrics
Passed: No visual artifacts and/or the comparison with the reference data near or above the specification.
Failed: Cause of performance degradation is unknown.
The comparisons with the reference data are computed over all data.
20

## Slide 21: PROVISIONAL VALIDATION PRODUCT MATURITY ASSESSMENT
GOES-16 ABI L2 LAP Product Provisional PS-PVR

## Slide 22: Examples of Visual Inspection of All Domains
22

## Slide 23: PLPT ABI-FD-TPW, LVT, LVM:
July 01, 2017, 2000 UTC
PASSED
TPW (mm)
Temp (K). 500 hPa hPa
WV (g/kg) 850 hPa
23
TPW: Total Precipitable Water
LVT: Legacy Vertical Temperature profile
LVM: Legacy Vertical Moisture profile

## Slide 24: PLPT ABI-FD-DSI:
July 01, 2017, 2000 UTC
PASSED
LI
CAPE
TT
KI
SI
24
LI: Lifted Index
CAPE: Convective Available Potential Energy
TT: Total Totals
KI: K-Index
SI: Showalter Index

## Slide 25: PLPT ABI-CONUS-TPW, LVT, LVM:
PASSED
July 01, 2017, 2002 UTC
25
TPW (mm)
Temp (K). 500 hPa hPa
WV (g/kg) 850 hPa
TPW: Total Precipitable Water
LVT: Legacy Vertical Temperature profile
LVM: Legacy Vertical Moisture profile

## Slide 26: PLPT ABI-CONUS-DSI:
July 01, 2017, 2002 UTC
PASSED
LI
CAPE
KI
SI
TT
26
LI: Lifted Index
CAPE: Convective Available Potential Energy
TT: Total Totals
KI: K-Index
SI: Showalter Index

## Slide 27: PLPT ABI-MESO1-TPW, LVT, LVM:
PASSED
July 01, 2017, 2000 UTC
27
TPW (mm)
Temp (K). 500 hPa hPa
WV (g/kg) 850 hPa
TPW: Total Precipitable Water
LVT: Legacy Vertical Temperature profile
LVM: Legacy Vertical Moisture profile

## Slide 28: PLPT ABI-MESO1-DSI:
July 01, 2017, 2000 UTC
PASSED
LI
CAPE
KI
SI
TT
28
LI: Lifted Index
CAPE: Convective Available Potential Energy
TT: Total Totals
KI: K-Index
SI: Showalter Index

## Slide 29: PLPT ABI-MESO2-TPW, LVT, LVM:
PASSED
July 01, 2017, 2000 UTC
29
TPW (mm)
Temp (K). 500 hPa hPa
WV (g/kg) 850 hPa
TPW: Total Precipitable Water
LVT: Legacy Vertical Temperature profile
LVM: Legacy Vertical Moisture profile

## Slide 30: PLPT ABI-MESO2-DSI:
July 01, 2017, 2000 UTC
PASSED
LI
CAPE
KI
SI
TT
30
LI: Lifted Index
CAPE: Convective Available Potential Energy
TT: Total Totals
KI: K-Index
SI: Showalter Index

## Slide 31: Locations of Suomi-Net GPS and RAOB
Suomi-Net GPS
RAOB (red) and AERI (blue)
31
Notes: On the left figure, all the red dots indicate SuomiNet-GPS locations and the blue dot in Dominican Republic (lat: 18.79, lon: -70.66) indicates the location
where most of the outliers in tpw figures are located.
On the right figure, all the red dots indicate RAOB locations and the blue dot near the Michigan Lake (lat: 43.75, lon: -87.71) indicates AERI observation.

## Slide 32: Comparison TPW with the GPS, RAOB, AMSR2, ECMWF, and GDAS
32
Note that ECMWF and GDAS data are new in the LAP provisional validation.
Both GDAS and ECMWF analysis have 0.25o X 0.25o resolution.

## Slide 33: Requirements for ABI Legacy Atmospheric Profile (LAP) products
Product | Accuracy | Precision | Range
Temperature | 1 K below 400 hPa and above boundary layer | 2 K below 400 hPa and above boundary layer | 180 - 320 K
Moisture | Sfc - 300 hPa: 18% 300 - 100 hPa: 20% | Sfc-300 hPa: 18% 300-100 hPa: 20% | 0 - 100%
TPW | 1 mm | 3 mm | 0 - 100 mm
Lifted index | 2.0 K | 6.5 K | -10 ~ 40 K or above
CAPE | 1000 J/kg | 2500 J/kg | 0 - 5000 J/kg
SSI | 2.0 K | 6.5 K | -10 ~ 4 K or above
TT | 1 K | 4 K | -43 ~ 56 K
K index | 2 K | 5 K | 0 - 40 K
33

## Slide 34: PLPT ABI-FD-TPW:
GPS
RAOB
AMSR2
PASSED
2017.04-2018.01
34
Accuracy spec: 1 mm
Precision spec: 3 mm

## Slide 35: PLPT ABI-FD-TPW:
ECMWF
GDAS
PASSED
2017.05-2018.01
35
Accuracy spec: 1 mm
Precision spec: 3 mm

## Slide 36: PLPT ABI-CONUS-TPW:
GPS
RAOB
AMSR2
PASSED
2017.04-2018.01
36
Accuracy spec: 1 mm
Precision spec: 3 mm

## Slide 37: PLPT ABI-CONUS-TPW:
ECMWF
GDAS
PASSED
2017.05-2018.01
37
Accuracy spec: 1 mm
Precision spec: 3 mm

## Slide 38: PLPT ABI-MESO1-TPW:
GPS
RAOB
AMSR2
PASSED
2017.04-2018.01
38
Accuracy spec: 1 mm
Precision spec: 3 mm

## Slide 39: PLPT ABI-MESO1-TPW:
ECMWF
GDAS
PASSED
2017.05-2018.01
39
Accuracy spec: 1 mm
Precision spec: 3 mm

## Slide 40: PLPT ABI-MESO2-TPW:
GPS
RAOB
AMSR2
PASSED
2017.04-2018.01
40
Accuracy spec: 1 mm
Precision spec: 3 mm

## Slide 41: PLPT ABI-MESO2-TPW:
ECMWF
GDAS
PASSED
2017.05-2018.01
41
Accuracy spec: 1 mm
Precision spec: 3 mm

## Slide 42: PLPT ABI-FD-DSI:
PASSED
2017.06 GPS, outliers over CN06
Accuracy: -0.26 mm
Precision: 3.13 mm
Sample Size: 906864
Accuracy: -0.28 mm
Precision: 3.07 mm
Sample Size: 905772
Most of the outliers are located at the GPS location (CN06, Dominican Republic lat:18.79, lon: -70.66). The number of pixels over CN06 is around 0.1% of the total number of the collocated pixels between GPS and GOES-16 baseline TPW.
42
Notes: Most of the outliers are located at the GPS location (CN06, Dominican Republic lat:18.79, lon: -70.66) .
The number of pixels over CN06 is around 0.1% of the total number of the collocated pixels between GPS and baseline TPW.

## Slide 43: Comparisons with GOES-15 Sounder (Case study)
The period includes September, October and November of 2017.
The overlapped TPW regions between GOES-15 Sounder and GOES-16 ABI are CONUS and full disk sectors.
ABI baseline and GOES-15 Sounder TPW products are compared with GPS TPW; they are close and comparable, both meet the requirement.

## Slide 44
Full disk and GOES-15
CONUS and GOES-15
GOES-15 vs. GOES-16 ABI TPW overlapped coverage

## Slide 45
Baseline (ABI) vs. GOES-15 TPW
comparison with GPS TPW
Full Disk
CONUS
Accuracy spec: 1 mm
Precision spec: 3 mm

## Slide 46: TPW Performance Summary
TPW retrieval is working as expected on GOES-16 ABI data when combined with NWP short-rang forecasts (as first guess);
With a quantitative web-based tool (http://soundingval.ssec.wisc.edu) and the comparisons with RAOB, AMSR2, GPS, ECMWF and GDAS, it does indicate performances meet spec. for all the coverages (FD, CONUS, Meso1, and Meso2), except several Meso1 and Meso2 cases which do not have enough number of samples or where mean TPW is comparatively large.
For the comparisons with GPS TPW, most of the outliers are located over CN06 (lat: 18.79, lon: -70.66).
46

## Slide 47
Real-time GOES-16 ABI LAP product validation webpage soundingval.ssec.wisc.edu
Imagery (Fulldisk TPW)
Station TPW Plots with deep dive capability
Regional Plots with GPS

## Slide 48: Comparison LVT & LVM with the RAOB, ECMWF, GDAS, and field campaign (AERI)
48
Note that ECMWF, GDAS, AERI data are new in the LAP provisional validation.

## Slide 49: Requirements for ABI Legacy Atmospheric Profile (LAP) products
Product | Accuracy | Precision | Range
Temperature | 1 K below 400 hPa and above boundary layer | 2 K below 400 hPa and above boundary layer | 180 - 320 K
Moisture | Sfc - 300 hPa: 18% 300 - 100 hPa: 20% | Sfc - 300 hPa: 18% 300 - 100 hPa: 20% | 0 - 100%
TPW | 1 mm | 3 mm | 0 - 100 mm
Lifted index | 2.0 K | 6.5 K | -10 ~ 40 K or above
CAPE | 1000 J/kg | 2500 J/kg | 0 - 5000 J/kg
SSI | 2.0 K | 6.5 K | -10 ~ 4 K or above
TT | 1 K | 4 K | -43 ~ 56 K
K index | 2 K | 5 K | 0 - 40 K
49

## Slide 50: PLPT ABI-FD, CONUS-LVT, LVM:
PASSED
2017.05-2018.01 RAOB
Temperature (K)
Full Disk
Relative Humidity (%)
CONUS
Sample Size: 21705
Sample Size: 28451
Sample Size: 28451
50
Sample Size: 21705
Accuracy spec:
1 K (BL-400hPa)
Precision spec:
2 K (BL-400hPa)
Accuracy & Precision spec:
18% (sfc-300hPa), 20% (300-100hPa)
Notes: Sample size is “maximum”, eg, if one level has a match.

## Slide 51: PLPT ABI-FD, CONUS-LVT, LVM:
PASSED
2017.06.01 00UTC ECMWF
Temperature (K)
Full Disk
Relative Humidity (%)
CONUS
Sample Size: 56254
Sample Size: 378863
Sample Size: 378863
51
Sample Size: 56254
Accuracy spec:
1 K (BL-400hPa)
Precision spec:
2 K (BL-400hPa)
Accuracy & Precision spec:
18% (sfc-300hPa), 20% (300-100hPa)

## Slide 52: PLPT ABI-FD, CONUS-LVT, LVM:
PASSED
2017.06.01 00UTC GDAS
Temperature (K)
Full Disk
Relative Humidity (%)
CONUS
Sample Size: 56254
Sample Size: 378863
Sample Size: 378863
52
Sample Size: 56254
Accuracy spec:
1 K (BL-400hPa)
Precision spec:
2 K (BL-400hPa)
Accuracy & Precision spec:
18% (sfc-300hPa), 20% (300-100hPa)

## Slide 53: PLPT ABI-FD, CONUS-LVT, LVM:
PASSED
2017.05.22 – 06.22 AERI (lat:43.75 lon:-87.71)
Temperature (K)
Full Disk
Relative Humidity (%)
CONUS
Sample Size: 4393
Sample Size: 1289
Sample Size: 1289
53
Sample Size: 4394
Accuracy spec:
1 K (BL-400hPa)
Precision spec:
2 K (BL-400hPa)
Accuracy & Precision spec:
18% (sfc-300hPa), 20% (300-100hPa)
Notes: AERI measurements are valid upto around 700 hPa.

## Slide 54: PLPT ABI-Meso1, Meso2-LVT, LVM:
PASSED
Temperature (K)
Sample Size: 1720
Meso1
Relative Humidity (%)
Meso2
Sample Size: 1720
Sample Size: 1853
2017.05-2018.01 RAOB
54
Sample Size: 1853
Accuracy spec:
1 K (BL-400hPa)
Precision spec:
2 K (BL-400hPa)
Accuracy & Precision spec:
18% (sfc-300hPa), 20% (300-100hPa)

## Slide 55: PLPT ABI-Meso1, Meso2-LVT, LVM:
PASSED
Temperature (K)
Sample Size: 3100
Meso1
Relative Humidity (%)
Meso2
Sample Size: 3100
Sample Size: 6438
2017.06.01 00UTC ECMWF
55
Sample Size: 6438
Accuracy spec:
1 K (BL-400hPa)
Precision spec:
2 K (BL-400hPa)
Accuracy & Precision spec:
18% (sfc-300hPa), 20% (300-100hPa)

## Slide 56: PLPT ABI-Meso1, Meso2-LVT, LVM:
PASSED
Temperature (K)
Sample Size: 3100
Meso1
Relative Humidity (%
Meso2
Sample Size: 3100
Sample Size: 6438
2017.06.01 00UTC GDAS
56
Sample Size: 6438
Accuracy spec:
1 K (BL-400hPa)
Precision spec:
2 K (BL-400hPa)
Accuracy & Precision spec:
18% (sfc-300hPa), 20% (300-100hPa)

## Slide 57: PLPT ABI-Meso1, Meso2-LVT, LVM:
2017.05.22 – 06.22 AERI (lat:43.75 lon:-87.71)
PASSED
Temperature (K)
Sample Size: 358
Meso1
Relative Humidity (%)
Meso2
Sample Size: 358
Sample Size: 6770
57
Sample Size: 6770
Accuracy spec:
1 K (BL-400hPa)
Precision spec:
2 K (BL-400hPa)
Accuracy & Precision spec:
18% (sfc-300hPa), 20% (300-100hPa)
Notes: AERI measurements are valid upto around 700 hPa.

## Slide 58: LVT and LVM Performance Summary
LVT and LVM retrievals are working as expected on GOES-16 ABI data when combined with NWP short-range forecasts (as first guess);
Retrievals are sensitive to first guess;
With a highly quantitative web-based tool (http://soundingval.ssec.wisc.edu) and the comparisons with RAOB, ECMWF, GDAS, and AERI measurements from GOES-R field campaign (Lake Michigan Ozone Study - LMOS 2017: https://www-air.larc.nasa.gov/missions/lmos/), it does indicate that performances meet spec. for all the coverages (FD, CONUS, Meso1, Meso2), except the relative humidity at upper troposphere (100 - 300 hPa) when compared with RAOB, which is likely due to the known issue of dry bias of radiosonde observations.
58

## Slide 59: Comparison DSI with the RAOB, ECMWF, and GDAS
59
Note that ECMWF, GDAS data are new in the LAP provisional validation.

## Slide 60: Requirements for ABI Legacy Atmospheric Profile (LAP) products
Product | Accuracy | Precision | Range
Temperature | 1 K below 400 hPa and above boundary layer | 2 K below 400 hPa and above boundary layer | 180 - 320 K
Moisture | Sfc - 300 hPa: 18% 300 - 100 hPa: 20% | Sfc - 300 hPa: 18% 300 - 100 hPa: 20% | 0 - 100%
TPW | 1 mm | 3 mm | 0 - 100 mm
Lifted index | 2.0 K | 6.5 K | -10 ~ 40 K or above
CAPE | 1000 J/kg | 2500 J/kg | 0 - 5000 J/kg
SSI | 2.0 K | 6.5 K | -10 ~ 4 K or above
TT | 1 K | 4 K | -43 ~ 56 K
K index | 2 K | 5 K | 0 - 40 K
60

## Slide 61: PLPT ABI-FD-DSI:
PASSED
LI
CAPE
TT*
2017.04-2018.01 RAOB
61
Accuracy spec: 2 K
Precision spec: 6.5 K
Accuracy spec: 1000 J/kg
Precision spec: 2500 J/kg
Accuracy spec: 1 K
Precision spec: 4 K
*TT results are slightly larger than spec when compared with RAOBs during this time of non-operational ABI data. Of course RAOB are point data, compared to NWP models.

## Slide 62: PLPT ABI-FD-DSI:
PASSED
KI*
SI
2017.04-2018.01 RAOB
62
Accuracy spec: 2 K
Precision spec: 5 K
Accuracy spec: 2 K
Precision spec: 6.5 K
*KI results are a bit larger than spec when compared with RAOBs during this time of non-operational ABI data. RAOB are point data, compared to NWP models. See next slide for more analysis

## Slide 63: PLPT ABI-FD-CONUS-DSI:
PASSED
KI (>26 for unstable cases)
TT (>44 for unstable cases)
2017.04-2018.01 RAOB
including “only unstable cases”
Full Disk
CONUS
63
Accuracy spec: 2 K
Precision spec: 5 K
Accuracy spec: 1 K
Precision spec: 4 K
Accuracy spec: 2 K
Precision spec: 5 K
Accuracy spec: 1 K
Precision spec: 4 K
Notes: Considering only unstable cases, most of the accuracy and precision of TT and KI are reduced in magnitude.

## Slide 64: PLPT ABI-FD-DSI:
PASSED
LI
CAPE
TT
2017.05-2017.12 ECMWF
64
Accuracy spec: 2 K
Precision spec: 6.5 K
Accuracy spec: 1000 J/kg
Precision spec: 2500 J/kg
Accuracy spec: 1 K
Precision spec: 4 K

## Slide 65: PLPT ABI-FD-DSI:
PASSED
KI
SI
2017.05-2017.12 ECMWF
65
Accuracy spec: 2 K
Precision spec: 5 K
Accuracy spec: 2 K
Precision spec: 6.5 K

## Slide 66: PLPT ABI-FD-DSI:
PASSED
LI
CAPE
TT
2017.05-2018.01 GDAS
66
Accuracy spec: 2 K
Precision spec: 6.5 K
Accuracy spec: 1000 J/kg
Precision spec: 2500 J/kg
Accuracy spec: 1 K
Precision spec: 4 K

## Slide 67: PLPT ABI-FD-DSI:
PASSED
KI
SI
2017.05-2018.01 GDAS
67
Accuracy spec: 2 K
Precision spec: 5 K
Accuracy spec: 2 K
Precision spec: 6.5 K

## Slide 68: PLPT ABI-CONUS-DSI:
PASSED
LI
CAPE
TT
2017.04-2018.01 RAOB
68
Accuracy spec: 2 K
Precision spec: 6.5 K
Accuracy spec: 1000 J/kg
Precision spec: 2500 J/kg
Accuracy spec: 1 K
Precision spec: 4 K

## Slide 69: PLPT ABI-CONUS-DSI:
PASSED
KI
SI
2017.04-2018.01 RAOB
69
Accuracy spec: 2 K
Precision spec: 5 K
Accuracy spec: 2 K
Precision spec: 6.5 K

## Slide 70: PLPT ABI-CONUS-DSI:
PASSED
LI
CAPE
TT
2017.05-2017.12 ECMWF
70
Accuracy spec: 2 K
Precision spec: 6.5 K
Accuracy spec: 1000 J/kg
Precision spec: 2500 J/kg
Accuracy spec: 1 K
Precision spec: 4 K

## Slide 71: PLPT ABI-CONUS-DSI:
PASSED
KI
SI
2017.05-2017.12 ECMWF
71
Accuracy spec: 2 K
Precision spec: 5 K
Accuracy spec: 2 K
Precision spec: 6.5 K

## Slide 72: PLPT ABI-CONUS-DSI:
PASSED
LI
CAPE
TT
2017.05-2018.01 GDAS
72
Accuracy spec: 2 K
Precision spec: 6.5 K
Accuracy spec: 1000 J/kg
Precision spec: 2500 J/kg
Accuracy spec: 1 K
Precision spec: 4 K

## Slide 73: PLPT ABI-CONUS-DSI:
PASSED
KI
SI
2017.05-2018.01 GDAS
73
Accuracy spec: 2 K
Precision spec: 5 K
Accuracy spec: 2 K
Precision spec: 6.5 K

## Slide 74: PLPT ABI-MESO1-DSI:
PASSED
LI
CAPE
TT
2017.04-2018.01 RAOB
74
Accuracy spec: 2 K
Precision spec: 6.5 K
Accuracy spec: 1000 J/kg
Precision spec: 2500 J/kg
Accuracy spec: 1 K
Precision spec: 4 K

## Slide 75: PLPT ABI-MESO1-DSI:
PASSED
KI
SI
2017.04-2018.01 RAOB
75
Accuracy spec: 2 K
Precision spec: 5 K
Accuracy spec: 2 K
Precision spec: 6.5 K

## Slide 76: PLPT ABI-MESO1-DSI:
PASSED
LI
CAPE
TT
2017.05-2017.12 ECMWF
76
Accuracy spec: 2 K
Precision spec: 6.5 K
Accuracy spec: 1000 J/kg
Precision spec: 2500 J/kg
Accuracy spec: 1 K
Precision spec: 4 K

## Slide 77: PLPT ABI-MESO1-DSI:
PASSED
KI
SI
2017.05-2017.12 ECMWF
77
Accuracy spec: 2 K
Precision spec: 5 K
Accuracy spec: 2 K
Precision spec: 6.5 K

## Slide 78: PLPT ABI-MESO1-DSI:
PASSED
LI
CAPE
TT
2017.05-2018.01 GDAS
78
Accuracy spec: 2 K
Precision spec: 6.5 K
Accuracy spec: 1000 J/kg
Precision spec: 2500 J/kg
Accuracy spec: 1 K
Precision spec: 4 K

## Slide 79: PLPT ABI-MESO1-DSI:
PASSED
KI
SI
2017.05-2018.01 GDAS
79
Accuracy spec: 2 K
Precision spec: 5 K
Accuracy spec: 2 K
Precision spec: 6.5 K

## Slide 80: PLPT ABI-MESO2-DSI:
PASSED
LI
CAPE
TT
2017.04-2018.01 RAOB
80
Accuracy spec: 2 K
Precision spec: 6.5 K
Accuracy spec: 1000 J/kg
Precision spec: 2500 J/kg
Accuracy spec: 1 K
Precision spec: 4 K

## Slide 81: PLPT ABI-MESO2-DSI:
PASSED
KI
SI
2017.04-2018.01 RAOB
81
Accuracy spec: 2 K
Precision spec: 5 K
Accuracy spec: 2 K
Precision spec: 6.5 K

## Slide 82: PLPT ABI-MESO2-DSI:
PASSED
LI
CAPE
TT
2017.05-2017.12 ECMWF
82
Accuracy spec: 2 K
Precision spec: 6.5 K
Accuracy spec: 1000 J/kg
Precision spec: 2500 J/kg
Accuracy spec: 1 K
Precision spec: 4 K

## Slide 83: PLPT ABI-MESO2-DSI:
PASSED
KI
SI
2017.05-2017.12 ECMWF
83
Accuracy spec: 2 K
Precision spec: 5 K
Accuracy spec: 2 K
Precision spec: 6.5 K

## Slide 84: PLPT ABI-MESO2-DSI:
PASSED
LI
CAPE
TT
2017.05-2018.01 GDAS
84
Accuracy spec: 2 K
Precision spec: 6.5 K
Accuracy spec: 1000 J/kg
Precision spec: 2500 J/kg
Accuracy spec: 1 K
Precision spec: 4 K

## Slide 85: PLPT ABI-MESO2-DSI:
PASSED
KI
SI
2017.05-2018.01 GDAS
85
Accuracy spec: 2 K
Precision spec: 5 K
Accuracy spec: 2 K
Precision spec: 6.5 K

## Slide 86: DSI Performance Summary
DSI retrieval is working as expected on GOES-16 ABI data when combined with NWP short-range forecasts (as first guess);
With a highly quantitative web-based tool (http://soundingval.ssec.wisc.edu) and the comparisons with RAOB, ECMWF and GDAS, it does indicate performances mostly meet spec. for all the coverages, except comparisons of TT and KI with RAOBs. The TT and KK results are much closer to the requirements if the atmosphere is in the unstable conditions.
The beta-stage cloud mask was used for all retrievals.
86

## Slide 87: PLPT Outcomes: Summary
All PLPT activities needed to make LAP products provisional have been completed.
Recommendations from Beta review are fulfilled in the provisional validation stage.
Unexpected minor issues revealed by PLPTs:
  Missing values in random boxed areas
  The migration of the sun affects the LAP products.
  Slightly large discrepancy of some DSI products compared with RAOB.
These minor issues may not prevent the declaration of Provisional Maturity

## Slide 88: PATH TO FULL MATURITY
GOES-16 ABI L2 LAP Product Provisional PS-PVR

## Slide 89: Path to Full Maturity
We expect to apply the same PLPTs to be conducted for Full Maturity
  We are gathering an archive of golden days where we save L1,L2 and IPs.
  Our goal is extended period tests throughout May 2017 to May 2018.
  This collection is underway. Will coordinate with other teams.
  We are also saving L2 to enable further comparison with the reference datasets such as ECMWF and GDAS analysis data.
  We hope to engage the teams in the summer and begin application-specific analysis.
  Retrievals with the provisional cloud mask will be validated.
Currently minor issues may not prevent declaration of Full Maturity (3 issues identified through the PLPT work and will be mitigated during provisional stage)
  Missing values are randomly discovered over some boxed areas. This will be resolved when we transition from terrestrial GRB to RF GRB at NSOF. This is scheduled to occur by Handover.
  LAP products are affected by the migration of the sun which might be caused by the cloud mask.
  TT and KI values have slightly large discrepancy when compared with RAOBs; when considering only unstable atmospheric conditions, the results are closer to specification.

## Slide 90: Issue #1 – Missing data over randomly distributed boxed areas
Initial analysis showed missing data over randomly distributed boxed area
  The missing data occur frequently and randomly in boxed shapes
Notes: PRO team may clarify more about this.

## Slide 91: An example of the missing data in boxed area over Full disk

## Slide 92: An example of the missing data in boxed area over Full disk

## Slide 93: An example of the missing data in boxed area over Full disk

## Slide 94: Issue #2 – The migration of the sun affecting the LAP products
Initial analysis showed that the migration of the sun affects the LAP products.
  Some retrievals appear abnormal in sun-set and sun-rise regions.
Notes: PRO team may clarify more about this.

## Slide 95: An example of the migration of the sun affecting LAP products over Full Disk
Notes: Regions of sun-rise and sun-set are prone to this issue.

## Slide 96: An example of the migration of the sun affecting LAP products over Full Disk
Notes: Regions of sun-rise and sun-set are prone to this issue.

## Slide 97: Full Maturity PLPTs
Test ID | Test Title
ABI-FD_TPW12 | Assess the accuracy and precision of the TPW product for an extended period.
ABI-CONUS_TPW13 | Same as for ABI-FD_TPW12 except for CONUS.
ABI-MESO_TPW14 | Same as for ABI-FD_TPW12 except for Meso.
ABI-FD_LVT12 | Assess the accuracy and precision of the LVT product for an extended period.
ABI-CONUS_LVT13 | Same as for ABI-FD_LVT12 except for CONUS.
ABI-MESO_LVT14 | Same as for ABI-FD_LVT12 except for Meso.
ABI-FD_LVM12 | Assess the accuracy and precision of the LVM product for an extended period.
ABI-CONUS_LVM13 | Same as for ABI-FD_LVM12 except for CONUS.
ABI-MESO_LVM14 | Same as for ABI-FD_LVM12 except for Meso.
ABI-FD_DSI12 | Assess the accuracy and precision of the DSI product for an extended period.
ABI-CONUS_DSI13 | Same as for ABI-FD_DSI12 except for CONUS.
ABI-MESO_DSI14 | Same as for ABI-FD_DSI12 except for Meso.
AWG Sounding Team will conduct these tests to further evaluate the L2 TPW, LVT, LVM, and DSI product quality.
Full test plans and procedures are given in the INST Readiness, Implementation, and Management Plans (RIMP v1.0; 416-R-RIMP-0339, 0340, and 0341)

## Slide 98: Risks to Reaching Full Maturity
Risk Name | Description | Impact | Mitigation and Schedule
Missing values over randomly distributed areas | Frequently, there are missing values over randomly distributed boxed areas. | Minor | The filling values indicate no value regions. This is a result of using the terrestrial GRB at NSOF. Will be moving to RF GRB by Handover which will resolve this issue.
The migration of the sun affecting the LAP products | The ABI LAP products are affected by sun-rise and sun-set. | Minor | Cloud mask may have influences on the ABI LAP products.
Slightly large discrepancy of several DSI | Two DSI (TT and KI) show slightly larger discrepancy than the spec when compared to point-source raobs. | Minor | If the atmospheric conditions are unstable, the statistics results are closer to the requirements. Train forecasters to use the temporal and spatial gradients.
Little Impact
Moderate Impact
Large Impact

## Slide 99: Other concerns to Full Maturity
CAPE method in GOES-R LAP is based on MLCAPE (mixed layer) which might be different from other CAPE products forecasters compare to.
Need to output the surface pressure.
Layered PW (LPW) should be considered in the enhanced products based on the feedback from forecasters during HWT demonstration.
Notes: HWT – Hazardous Weather Testbed

## Slide 100
SBCAPE vs. MLCAPE
SPC mesoscale analysis & ABI
SBCAPE: red contours
SPC
MLCAPE: red contours
SPC
Usually, MLCAPE is much lower than SBCAPE due to the averaging
SBCAPE: surface-based CAPE
MLCAPE: mean-layer CAPE (lowest 100 hPa layer)
Currently, the ABI baseline CAPE is based on MLCAPE.
ABI CAPE

## Slide 101: SUMMARY AND RECOMMENDATIONS
GOES-16 ABI L2 LAP Product Provisional PS-PVR

## Slide 102: Summary
AWG LAP team has validated GOES-16 LAP products (TPW, LVT, LVM, DSI) from April 2017 to January 2018 with various reference data (RAOB, Suomi-Net GPS, ECMWF analysis, GDAS, AMSR2, GOES-15 Sounder and AERI from field campaign) in real-time, the performance meet the requirements;
AWG LAP team recommend that TPW, LVT, LVM, and DSI products be transitioned to Provisional status at this time;
AWG LAP team have found the following minor issues which should not prevent Provisional status
  Missing values occur frequently and randomly over boxed areas.
  The migration of the sun affects the LAP products via cloud mask.
  Comparisons of TT and KI with RAOBs shows a little larger than spec. The TT and KK results are much closer to the requirements when compared with RAOBs if the atmosphere is in the unstable conditions.