## Slide 1: EHIS PS-PVR SWPC Overview
EHIS is performing best in the area where its contribution is unique and most important among SEISS sensors: heavy ion fluxes (carbon to iron) during SEP events
SWPC supports transitioning of EHIS L1b to Provisional status, understanding that continued mitigation and validation effort is needed
Shortfalls in other areas (helium, hydrogen, GCR heavies) need to be addressed
  Currently SWPC has a planned L2 product that transforms flux vs. energy spectra to flux vs. linear-energy-transfer (LET) spectra, as requested by the satellite engineering community – accurate input fluxes are needed for this product
SWPC concurs with NCEI recommendations to consider the following:
  Refine flight tables to improve histogram-based retrieval of heavy ion fluxes
  If a solution cannot be found for the EHIS helium problem, implement real-time processing of SGPS alpha channels
  Implement L1b temperature correction of EHIS hydrogen channels following development and testing by NCEI
  Implement alternative logic in GOES-17 EHIS to enable on-orbit comparison of different H and He response functions

## Slide 2: SGPS PS-PVR SWPC Overview
Overall SGPC is performing well, but there are some anomalous SGPS channels with unknown root cause and/or path to resolution (e.g., SGPS+X P7).
Steps to mitigate effect of anomalous channels on data accuracy and SPE detection
  Implement temperature correction and characterize its impact.
  Implement corrections to anomalous SGPS channels.
  Assess impacts of temperature dependence and anomalous channels on data accuracy and SPE detection.
  Where needed, consider contingency operations.
SWPC is highly appreciative of the excellent work and diligence provided by NCEI, as well as the support provided by ATC and the entire GOES project.
SWPC concurs with NCEI’s recommendation for SGPS L1b to transition to provisional status, with understanding that testing, tuning, and assessment are still required.