## Slide 1: Peer Stakeholder-Product Validation Review (PS-PVR) For the Full Maturity of GOES-16 and GOES-17 SEISS MPS-HI L1b Product
October 13, 2021
GOES-R Calibration Working Group (CWG)
Presenter: Athanasios Boudouridis
Contributors: Juan Rodriguez, Brian Kress, Kevin Hallock, William Rowland
CIRES and NOAA NCEI
The NCEI team wish to thank the MPS-HI vendor Assurance Technology Corporation, the MIT Lincoln Labs, the Space Weather Prediction Center, and the GOES-R Program

## Slide 2: Outline
Review of Provisional Maturity
  Provisional ADR/WR status
  PLPTs for Full Maturity
Product Quality Evaluation
  Status at Full Validation Review
  Major Issues Remaining
Full Maturity Assessment
  Status
  Performance
  Risks
Summary and Recommendations
Backup slides

## Slide 3: Magnetospheric Particle Sensor – High Energy (MPS-HI)
Credit: SEISS-TR-MH074-2 Rev C, Figure 3-1
Primary purpose: measure radiation belt particle fluxes in the energy range responsible for internal charging
5 electron telescopes and 5 proton telescopes
  30 deg full-width conical FOVs, centers separated by 35 deg
Each electron telescope:
  10 differential channels, 50 keV – 4 MeV
  2 integral channels, >2 MeV and >4 MeV (latter not part of L1b)
Each proton telescope:
  11 differential channels
  7 channels, 80 keV – 1 MeV (trapped)
  4 channels, 1-12 MeV (solar protons)
Two dosimeters (250 and 100 mil Al)
  Distinguish particles depositing < 1 MeV and >1 MeV
MRD 3.3.6.1.3 Magnetospheric Electrons and Protons: Medium and High Energy

## Slide 4: ALERT: Electron 2 MeV Integral Flux exceeded 1000 pfu
SWPC alert at 1000 electrons/(cm2 sr s) [pfu] was developed in consultation with the satellite industry
Based on GOES-East observations
  Fluxes systematically lower than at GOES-West by factor of 2.5 [Meredith et al., 2015]
First alert issued 18 May 1995
In this otherwise quiet solar cycle, MeV electron fluxes have been very elevated starting in 2015
  Primarily owing to the action of stream interaction regions (interface between solar wind of coronal hole and quiet sun origins) on the magnetosphere
Space Weather Message Code: ALTEF3 Serial Number: 2516 Issue Time: 2017 Jan 09 0501 UTC
CONTINUED ALERT: Electron 2MeV Integral Flux exceeded 1000pfu Continuation of Serial Number: 2515 Begin Time: 2017 Jan 05 1520 UTC Yesterday Maximum 2MeV Flux: 25537 pfu www.swpc.noaa.gov/noaa-scales-explanation Potential Impacts: Satellite systems may experience significant charging resulting in increased risk to satellite systems.

## Slide 5
Proton differential flux
  Possible proton channel degradation
  Continues to date
  Compare with GOES-T data after launch
Proton contamination of electron channels
  No electron channel contamination observed in recent SEP event
  Electron detector design successful
  Strong SEP event required for definitive answer (NCEI will continue monitoring)
G16, G17 E11 fluxes
  G17/G16 E11 ratios consistent with different spacecraft location, radiation environment
G16 P1 channel calibration
  G16 P1 channel reported out of family with the rest of the G16 proton channels, higher than G17 P1 channel
  Compare with GOES-T data after launch
Solar Proton channels
  MPS-HI channels P9-P11 not in agreement with SGPS P2-P4
  Requires beam calibration (has been agreed by the program, to be planned by ATC)
GOES-16: Status at Full Review
Summary

## Slide 6
Proton differential flux
  Possible proton channel degradation
  Continues to date
  Compare with GOES-T data after launch
Proton contamination of electron channels
  No electron channel contamination observed in recent SEP event
  Electron detector design successful
  Strong SEP event required for definitive answer (NCEI will continue monitoring)
G16, G17 E11 fluxes
  G17/G16 E11 ratios consistent with different spacecraft location, radiation environment
Solar Proton channels
  Status not known due to lack of suitable SEP events for cross-comparison
  Requires an SEP event during active geomagnetic conditions to achieve isotropic particle distribution
GOES-17: Status at Full Review
Summary

## Slide 7: Review of PROVISIONAL Maturity
GOES-16 and GOES-17 MPS-HI L1b Products Full PS-PVR

## Slide 8: Product review for Full
Risks and associated ADRs identified at Provisional Validation Review
  Description
  Current status
PLPTs for Full Maturity
  PLPT-SEI-002: MPS-HI Telescope Cross-Comparison
  PLPT-SEI-004: Solar Energetic Particle (SEP) Cross-Comparison
  PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles
  PLPT-SEI-006: Backgrounds

## Slide 9: Instrument/GPA Issues Identified and Progress Status: MPS-HI
At Provisional PS-PVR, NCEI-CO recommended that these issues be investigated prior to declaring the GOES-16/-17 MPS-HI data of Full maturity.
ADR# | WR# | Short Description | Current Status | Expected Closure
700 | 6115 | Yaw Flip Flag incorrect for SEISS MPS-HI products | Closed | DO.07.01.00
780 | 6568 6845 | G16 & G17 MPS-HI and MPS-LO L1b IFC Leakage | Fix Fail In Analysis | DO.09.01.00 TBD
781 | 6477 8404 | G17 & G17 MPS-HI and SGPS L1b data gaps near IFCs | Fixed In Analysis | DO.09.02.00 TBD
863 | 6736 | Graceful degradation when SGPS data not generated | On Hold | TBD
845 | 6854 | Update PUG with SEISS MPS-HI and MPS-LO Angular Zone Info | Closed | PUG Update Revision H
872 | 6600 7056 | Solar array current not correct in G17 products | In Analysis On Hold | TBD

## Slide 10: ADR 780: G16 & G17 MPS-HI and MPS-LO L1b IFC leakage
MPS-HI problem description: IFC pulses are leaking into L1b proton fluxes
  G17 channel P1 before June 11, and G16 P1 currently
  On June 11, 2018, revised G17 (FM2) MPS-HI IFC table uploaded as part of PLT SEI-003 – moved problem from channel P1 to channels P6 & P7
    Strongly evident in 1-minute averages
  Occurs at end of periods when MODE flag set to 4
    MODE = 4 used to mask IFCs, set L1b Instrument_Mode flag
    IFC pulses last 1-2 seconds beyond MODE = 4
  Not observed in other proton channels or in electron channels
  Violates accuracy requirement

## Slide 11: ADR 780: Original Observations
25 June 2018, 1805-1825 UT, 1-second data: MODE = 4 pulse ends 2 seconds early, causing part of the second IFC pulse to be included in the L1b fluxes (indicated by solid arrows).
Top to Bottom: the Mode flag, then alternating L0 counts and L1b fluxes in this channel from Telescopes 1 through 5
Gaps after IFC are addressed by ADR 781

## Slide 12: ADR 780: Update and current status
After an initial attempt, ADR 780 (WR 6568) was designated a “fix failure” as the IFC leakage remained
WR 6845 was initiated to revisit
As of 09/20/2021 a remedy has been identified and work on ADR 780 is proceeding

## Slide 13: ADR 781: G16 & G17 MPS-HI and SGPS L1b data gaps near IFCs
Regular ~5-min gaps in MPS-HI and SGPS L1b near in-flight calibrations (IFCs)
  These gaps are in addition to the L1b data gaps during IFCs, which are required and are based on instrument mode flag = 4
  Gaps are simultaneous in MPS-HI and SGPS data
  All channels and telescopes affected on both satellites
  L0 data are available and valid during these gaps
  No data (e.g., no fluxes, no quality flags) in affected granular L1b files except labels and global attributes
Diagnosis: when either SGPS is in IFC mode, downstream products (MPS-HI and the other SGPS) are not processed
  Owing to use of SGPS channels for contamination correction of a small fraction of the total SGPS & MPS-HI channels
A preferable approach is graceful degradation of downstream data products:
  The channels that require contamination correction will be somewhat degraded in the absence of the SGPS data undergoing IFC, but still usable
  The channels that do not require contamination correction will not be degraded

## Slide 14: ADR 781: G17 MPS-HI Protons (T2 P7) and SGPS+X (P1) (example, 25 June 2018)

## Slide 15: ADR 781: G17 MPS-HI Electrons (T2 E7) and SGPS-X (P1) (example, 25 June 2018)

## Slide 16: ADR 781: Update and current status
ADR 781 (WR 6477) was successful in dealing with the MPS-HI gaps during SGPS IFCs, but unsuccessful for SGPS IFC inter-dependencies
WR 8404 was initiated to revisit the SGPS data gaps
As of 09/16/2021 SGPS algorithm changes have been identified, and work on ADR 781 is ongoing
SGPS-X & SGPS+X IFCs
MPS-HI IFC
No MPS-HI data gap during SGPS IFCs

## Slide 17: ADR 863: Graceful degradation when SGPS data not generated
Four electron channels from MPS-HI use SGPS-X data for a contamination correction. The SGPS P5 channel uses data from the opposite SGPS for a contamination correction. If for some reason (like a sensor failure) no data are being generated from one of the SGPS units, then the dependent products should still be produced with only graceful degradation. This is needed for Full validation of MPS-HI and SGPS. This is a generalization of ADR 781.
Case 1: SGPS-X data are not being generated
  MPS-HI fluxes should be calculated as if SGPS-X fluxes were zero rather than missing -- graceful degradation of 4 electron channels.
  SGPS L1b should still be produced with SGPS-X being all fill and SGPS+X containing valid fluxes (SGPS+X P5 being calculated as if SGPS-X fluxes were zero rather than missing -- graceful degradation of P5).
Case 2: SGPS+X data are not being generated.
  MPS-HI fluxes should be produced, no dependence on SGPS+X, no degradation.
  SGPS L1b should still be produced with SGPS+X being all fill and SGPS-X containing valid fluxes (SGPS-X P5 being calculated as if SGPS+X fluxes were zero rather than missing -- graceful degradation of P5).
Case 3: neither SGPS+X nor SGPS-X data being generated
  MPS-HI fluxes should be calculated as if SGPS-X fluxes were zero rather than missing -- graceful degradation of 4 electron channels.
CAUTION: ADR 863 can become critical in case of catastrophic failure of SGPS. MPS-HI E11 channel will be lost even though it is still functioning.
Applies to both GOES-16 and GOES-17

## Slide 18: ADR 872: Solar array current not correct in G17 products
GOES-16 MPS-HI 2018-10-01 0300-0700
GOES-17 MPS-HI 2018-10-01 0300-0700
Solar Array Current Eclipse Flag
Not exclusively SEISS. Also affects EXIS instruments and MAG.

## Slide 19: Path to Full Validation - PLPTs
Title | Activity | Data Needed | Success Criteria
A.3.2 MPS-Hi Telescope Cross-Comparison [PLPT-SEI-002] | Determine the relative sensitivity/response among MPS-HI telescopes. Account for differences in channel energy responses. | Three months of continuous data. (MAG, MPS-HI) | [Full] Telescopes agree to within 25%.
A.3.4 SEP Channel Cross-Comparison [PLPT-SEI-004] | On-orbit cross-calibration of MPS-HI with SGPS 1-12 MeV protons, and with GOES 13-15 EPEAD. | Two Solar Energetic Particle (SEP) events. | [Full] Differences quantified on data taken through validation phase.
A.3.5 Cross Satellite Comparison of Trapped Particles [PLPT-SEI-005] | Identify time periods when the two satellites should be measuring the same population, and compare results. Comparisons can be based on the satellites being within 15 degrees longitude (especially while G17 and G15 are separated by <10 deg at 126-135W), or using a very long time period. | Three months of continuous data. (MAG, MPS-HI) | [Full] Differences quantified on data taken through validation phase.
A.3.6 Backgrounds Trending [PLPT-SEI-006] | Model GCR spectra (e.g., NASA JSC Badhwar-O’Neill 2014) put through a forward model derived from MPS-HI instrument response functions to estimate MPS-HI channel fluxes for comparison with observations. Watch for deviation between P11-based correction and actual backgrounds. | Four months of continuous data. (MPS-HI, SGPS) | [Full] Perform analysis during validation phase.
MPS-HI Full Validation PLPTs from RIMP v 1.1 (02 June 2016) are a continuation of those completed for Provisional. Green annotations based on experience with MPS-HI.

## Slide 20: Use of Reprocessed Data in Provisional Validation PLPTs
Due to the dates of changes to OE (ADR 407 for GOES-16, and ADR 762 for GOES-17), the Provisional Validation PLPTs used reprocessed data
We have reprocessed L0 data using software that has been demonstrated to reproduce L1b results to ‘machine precision’ (ADRs 407 and 762 verification)
This demonstrated equivalence allowed us to perform Provisional PLPTs using reprocessed MPS-HI data
Some of the Provisional PLPTs, shown again for the Full validation, are based on those reprocessed data
The additional post-provisional analysis was performed using averages of real-time L1b data

## Slide 21: Demonstration of equivalence of reprocessed NCEI data and OE L1b (ADRs 407 and 762)
Goal: verify that ADR 407 (GOES-16) and ADR 762 (GOES-17) were successfully implemented in OE
Compared to fluxes and flux errors calculated from L0 by NCEI
  MPS-HI and SGPS L0 data aggregated into separate day files
  L0 day files processed into L1b day files based on CDRL79/CDRL80
  MPS-HI electron fluxes were derived using the bowtie diagonal matrix
For each L1b file (30 samples per channel):
  Calculate ratio of OE to NCEI products (flux and flux error, both in flux units)
  Take mean and standard deviation of ratios
  This gives a mean and a standard deviation for each L1b file
  Ideally, mean = 1.0 and standard deviation = 0.0
Results are good: ratio mean = 1.0, ratio standard deviation = 0.0 or ~10-8 (latter observed when quantity involves special function such as square root)

## Slide 22: 6 November 2017
In general:
mean = 1.0
stdev ~ 10-8 or 0
Demonstration of equivalence of reprocessed NCEI data and OE L1b (ADRs 407, GOES-16)

## Slide 23
17 October
2018
In general:
mean = 1.0
stdev ~ 10-8 or 0
Demonstration of equivalence of reprocessed NCEI data and OE L1b (ADRs 762, GOES-17)

## Slide 24: PLPTs for Full Validation
PLPT-SEI-002: MPS-HI Telescope Cross-Comparison (Hallock, Rowland, Rodriguez)
PLPT-SEI-004: Solar Energetic Particle (SEP) Cross-Comparison – GOES-16 only, no suitable SEP events for cross-comparison since GOES-17 launch (Kress)
PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles (Rodriguez)
PLPT-SEI-006: Backgrounds (Rodriguez, Boudouridis)

## Slide 25: PLPT-SEI-002: MPS-HI Telescope Cross-Comparison: Method
Steps:
  Input MPS-HI fluxes and pitch angles calculated from MAG L1b BRF
  Identify whenever a pair of telescopes has pitch angles within 1 degree
    Fold pitch angles > 90 degrees to get enough matches
Ref: Rowland, W., and R. S. Weigel (2012), Intra-calibration of particle detectors on a three-axis stabilized geostationary platform, Space Weather, 10, S11002, doi:10.1029/2012SW000816.
  Report measured fluxes for each pitch angle match
  Estimate scaling factors with respect to a reference telescope
yaw flip
GOES-17
Compares responses of MPS-HI telescopes when central pitch angle is the same
Under such conditions, telescopes should be measuring the same flux for the same effective energy
The technique has been validated twice: 1) G17 MPS-LO zone intracal, and 2) G13/G15 MAGED/PD cross-telescope comparisons (Rodriguez et al., [2020], JSWSC)
Partial pass

## Slide 26
PLPT-SEI-002: MPS-HI Telescope Cross-Comparison: Improvements over Provisional
GOES-16 improvements
Larger data sample
Mag data at provisional maturity
Use of supplementary angles
Thresholding to eliminate low fluxes
GOES-17 improvements
Larger data sample
Mag data at provisional maturity
Remaining Caveats
Account for variation in channel energies across telescopes
GOES-17 Protons, April 2021
GOES-17 Electrons, April 2021

## Slide 27: PLPT-SEI-002: MPS-HI Telescope Cross-Comparison: GOES-16
Electron Scale Factors
January-May 2021
Blue: <10%, Green: 10-20%, Red: >20%
Proton Scale Factors
January-May 2021
Technique not applicable to solar proton channels P8-P11
Many more electron scale factors further from unity compared to provisional maturity.
Proton scale factors remain comparable.
Possible cause: Multi-layer insulation (MLI) degrades over time in space, causing a gradual change in the average temperature, that affects the solid state detectors.

## Slide 28: PLPT-SEI-002: MPS-HI Telescope Cross-Comparison: GOES-17
Electron Scale Factors
January-May 2021
Blue: <10%, Green: 10-20%, Red: >20%
Proton Scale Factors
January-May 2021
Technique not applicable to solar proton channels P8-P11
Electron scale factors remain good compared to provisional maturity.
Proton scale factors show some improvement compared to provisional maturity.
Question: How do these scale factors vary with time? Is there any trend?

## Slide 29: PLPT-SEI-002: MPS-HI Telescope Cross-Comparison: GOES-16
Electron Scale Factors
January-May 2021
Blue: <10%, Green: 10-20%, Red: >20%
ETel1/E6 scale factor in time
Always in the expected range
Calculate scale factors every month for a window of the next 3 months, 05/2018-03/2021.
Similar to the method of Rodriguez et al. [2020], JSWSC, applied to GOES-13/-15 data.

## Slide 30: PLPT-SEI-002: MPS-HI Telescope Cross-Comparison: GOES-16
Electron Scale Factors
January-May 2021
ETel2/E6 scale factor in time
Oscillating in and out the expected range
Blue: <10%, Green: 10-20%, Red: >20%
Calculate scale factors every month for a window of the next 3 months, 05/2018-03/2021.
Similar to the method of Rodriguez et al. [2020], JSWSC, applied to GOES-13/-15 data.

## Slide 31: PLPT-SEI-002: MPS-HI Telescope Cross-Comparison: GOES-16
Electron Scale Factors
January-May 2021
ETel3/E6 scale factor in time
Almost always out of the expected range
Blue: <10%, Green: 10-20%, Red: >20%
Calculate scale factors every month for a window of the next 3 months, 05/2018-03/2021.
Similar to the method of Rodriguez et al. [2020], JSWSC, applied to GOES-13/-15 data.

## Slide 32: PLPT-SEI-002: MPS-HI Telescope Cross-Comparison: GOES-16
Electron Summary, 05/2018-03/2021
Proton Summary, 05/2018-03/2021
Steady near 1
Steady near 1, with some exceptions
Variable, higher than 1
Steady near 1, except for P7
Steady near 1, except for P6, P7
Variable near 1, except P5
Oscillating, above 1

## Slide 33: PLPT-SEI-002: MPS-HI Telescope Cross-Comparison: GOES-17
Electron Summary, 01/2019-03/2021
Proton Summary, 05/2018-03/2021
Small variations around 1, T2 best, T5 worst
Electron application after provisional status
Steady decline toward 1, all telescopes

## Slide 34: PLPT-SEI-002: MPS-HI Telescope Cross-Comparison: Summary
Electrons:
  GOES-16 electron scale factors have deteriorated since Provisional, have moved away from unity
    Cautionary note 1: The GOES-16 Provisional scale factors were “optimally based on set of all matches (i.e. no reference telescope)”
    Cautionary note 2: They were also calculated on one month of data
    Possible root cause: Multi-layer insulation degrades over time in space
  GOES-17 electron scale factors remained close to unity
  Temporal evolution of scale factors exhibit big variations for GOES-16, and much smaller variations for GOES-17 (plot vertical scales different)
Protons:
  GOES-16 proton scale factors remain comparable to the ones from Provisional, both having big departures from unity
  GOES-17 proton scale factors are improved over Provisional
  Temporal evolution of scale factors exhibit stability for GOES-16, and trend toward unity for GOES-17
Partial pass

## Slide 35: PLPT-SEI-004: SEP Channel Cross-Comparison: MPS-HI P8-P11 and SGPS P1-P4
SGPS sensors look at east and west directions, MPS-HI telescopes look outward on a north/south fan. During periods of isotropic distributions all fluxes should be comparable.
MPS-HI proton fluxes are typically lower than those measured by SGPS (esp. P11).
MPS-HI is in better agreement with GOES-13 and -15 near 1-2 MeV.
SGPS is in better agreement with GOES-13 and -15 at higher energies.
GOES-16 SGPS/MPS-HI, GOES-13 and GOES-15 proton spectra from the July and Sept 2017 SEP events, during periods when an isotropic distribution is expected due to geomagnetic disturbance.
P8
P9
P10
P11
Partial pass

## Slide 36: PLPT-SEI-004: SEP Channel Cross-Comparison: MPS-HI P8 and SGPS P1 during a period of high solar wind dynamic pressure (isotropic distribution)
Period with SW Pdyn > 10 nPa
During geomagnetically quiet periods, the westward flux is higher than eastward flux, and MPS-HI flux lies in between.
(West)
(East)
At times of high solar wind dynamic pressure (Pdyn > 10 nPa), the “inside” and “outside” fluxes are approximately equal.
Rodriguez et al. (2010), The east‐west effect in solar proton flux measurements in geostationary orbit: A new GOES capability, Geophys. Res. Lett., Vol. 37, L07109, doi:10.1029/2010GL042531.
MPS-HI P8 and SGPS+X/-X P1 fluxes are in fair agreement.
GOES-16

## Slide 37: PLPT-SEI-004: SEP Channel Cross-Comparison: MPS-HI P11 and SGPS P4 during a period of high solar wind dynamic pressure
Period with SW Pdyn > 10 nPa
MPS-HI P11 much lower than SGPS+X/-X.
Too high Geometric Factor? Mischaracterized energy bands?
(West)
(East)
At times of high solar wind dynamic pressure (Pdyn > 10 nPa), the “inside” and “outside” fluxes are approximately equal.
Rodriguez et al. (2010), The east‐west effect in solar proton flux measurements in geostationary orbit: A new GOES capability, Geophys. Res. Lett., Vol. 37, L07109, doi:10.1029/2010GL042531.
Unexpected big difference between SGPS+X and -X. Incorrect Geometric Factors?
P9 and P10 comparisons in backup slides
GOES-16

## Slide 38: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Technique
Compare differential flux spectra from satellites separated by about 1 hour (or less) in local time (first 4 comparisons were made per-provisional):
  GOES-16 (89.5W) to GOES-13 (75.0W), 01/09/2017-10/31/2017
  GOES-16 (75.2W) to GOES-13 (74.5W), 12/11/2017-01/02/2018, near-conjunction
  GOES-17 (89.5W) to GOES-14 (105W), 06/20/2018-09/24/2018
  GOES-17 (89.5W) to GOES-16 (75.2W), 06/20/2018-09/24/2018
  GOES-17 (137.2W) to GOES-15 (128W), 03/28/2019-09/08/2019, conjunction, New!
Compare flux percentile spectra between telescopes of same orientation
  0, ±35, ±70 deg from zenith (radially outward)
MAGED (E, GdE) determined using same bowtie analysis / spectra as MPS-HI
Telescope order for the above comparisons
Partial pass

## Slide 39: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Results
GOES-16 vs GOES-13 Electrons
Telescope Order, North-to-South |  | 
MAGE/PD | MPS-HI E | MPS-HI P
9 | 3 | 1
6 | 1 | 4
1 | 4 | 2
8 | 2 | 5
7 | 5 | 3
Boudouridis, A., Rodriguez, J. V., Kress, B. T., Dichter, B. K., & Onsager, T. G. (2020). Development of a bowtie inversion technique for real‐time processing of the GOES‐16/‐17 SEISS MPS‐HI electron channels. Space Weather, 18, e2019SW002403. https://doi.org/10.1029/2019SW002403

## Slide 40: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Results
GOES-16 vs GOES-13 Electrons (near-conjunction)
Telescope Order, North-to-South |  | 
MAGE/PD | MPS-HI E | MPS-HI P
9 | 3 | 1
6 | 1 | 4
1 | 4 | 2
8 | 2 | 5
7 | 5 | 3
Boudouridis, A., Rodriguez, J. V., Kress, B. T., Dichter, B. K., & Onsager, T. G. (2020). Development of a bowtie inversion technique for real‐time processing of the GOES‐16/‐17 SEISS MPS‐HI electron channels. Space Weather, 18, e2019SW002403. https://doi.org/10.1029/2019SW002403
G13 e- spectra: low at lower energies, better agreement at higher energies

## Slide 41: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Results
GOES-16 vs GOES-13 Electrons, 01/09/2017– 10/31/2017
GOES-16 vs GOES-13 Electrons, 12/11/2017– 01/02/2018 (near-conjunction)
The comparisons are made by taking the ratio of the GOES‐13 to the GOES‐16 percentile fluxes, following interpolation to five common energies (80, 130, 180, 270, and 380 keV) assuming a piecewise power‐law distribution.
Boudouridis, A., Rodriguez, J. V., Kress, B. T., Dichter, B. K., & Onsager, T. G. (2020). Development of a bowtie inversion technique for real‐time processing of the GOES‐16/‐17 SEISS MPS‐HI electron channels. Space Weather, 18, e2019SW002403. https://doi.org/10.1029/2019SW002403

## Slide 42: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Results
Telescope Order, North-to-South |  | 
MAGE/PD | MPS-HI E | MPS-HI P
9 | 3 | 1
6 | 1 | 4
1 | 4 | 2
8 | 2 | 5
7 | 5 | 3
Contamination in MAGPD by MeV electrons?
GOES-16 vs GOES-13 Protons
MAGPD systematically low – due to radiation damage?
Other telescopes exhibit similar behavior, as can be seen in the G16 provisional PS-PVR.

## Slide 43: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Results
GOES-17 vs GOES-14 Electrons
Telescope Order, North-to-South |  | 
MAGE/PD | MPS-HI E | MPS-HI P
7 | 3 | 1
8 | 1 | 4
1 | 4 | 2
6 | 2 | 5
9 | 5 | 3
Boudouridis, A., Rodriguez, J. V., Kress, B. T., Dichter, B. K., & Onsager, T. G. (2020). Development of a bowtie inversion technique for real‐time processing of the GOES‐16/‐17 SEISS MPS‐HI electron channels. Space Weather, 18, e2019SW002403. https://doi.org/10.1029/2019SW002403
GOES-14 was inverted during this period, GOES-17 was upright.
G14 e- spectra: low at lower energies, better agreement at higher energies

## Slide 44: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Results
GOES-17 vs GOES-14 Electrons, 06/20/2018– 09/24/2018
The comparisons are made by taking the ratio of the GOES‐14 to the GOES‐17 percentile fluxes, following interpolation to five common energies (80, 130, 180, 270, and 380 keV) assuming a piecewise power‐law distribution.
Boudouridis, A., Rodriguez, J. V., Kress, B. T., Dichter, B. K., & Onsager, T. G. (2020). Development of a bowtie inversion technique for real‐time processing of the GOES‐16/‐17 SEISS MPS‐HI electron channels. Space Weather, 18, e2019SW002403. https://doi.org/10.1029/2019SW002403

## Slide 45: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Results
GOES-17 vs GOES-14 Protons
Telescope Order, North-to-South |  | 
MAGE/PD | MPS-HI E | MPS-HI P
7 | 3 | 1
8 | 1 | 4
1 | 4 | 2
6 | 2 | 5
9 | 5 | 3
G14 lower due to radiation damage
G14 discrepancy greater in T1 & T8 (closer to 90 deg pitch angle)
All G14 spectra show kink between MP3 and MP4
Other telescopes exhibit similar behavior, as can be seen in the G17 provisional PS-PVR.

## Slide 46: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Results
GOES-17 vs GOES-16 Electrons
Telescope Order, North-to-South |  | 
MAGE/PD | MPS-HI E | MPS-HI P
7 | 3 | 1
8 | 1 | 4
1 | 4 | 2
6 | 2 | 5
9 | 5 | 3
Boudouridis, A., Rodriguez, J. V., Kress, B. T., Dichter, B. K., & Onsager, T. G. (2020). Development of a bowtie inversion technique for real‐time processing of the GOES‐16/‐17 SEISS MPS‐HI electron channels. Space Weather, 18, e2019SW002403. https://doi.org/10.1029/2019SW002403
The reported fluxes are at residual background levels
The other G17 v G16 e- comparisons agree similarly well except ETel4
G16 e- ETel4 E3 fluxes and spectral shape are out-of-family

## Slide 47: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Results
GOES-17 vs GOES-16 Electrons, 06/20/2018– 09/24/2018
The comparisons are made by taking the ratio of the GOES‐16 to the GOES‐17 percentile fluxes, following interpolation to 10 common energies (80, 130, 180, 278, 380, 550, 900, 1,493, 1,969, and 2,890 keV) assuming a piecewise power‐law distribution.
Boudouridis, A., Rodriguez, J. V., Kress, B. T., Dichter, B. K., & Onsager, T. G. (2020). Development of a bowtie inversion technique for real‐time processing of the GOES‐16/‐17 SEISS MPS‐HI electron channels. Space Weather, 18, e2019SW002403. https://doi.org/10.1029/2019SW002403
E3 out of family

## Slide 48: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Results
Telescope Order, North-to-South |  | 
MAGE/PD | MPS-HI E | MPS-HI P
7 | 3 | 1
8 | 1 | 4
1 | 4 | 2
6 | 2 | 5
9 | 5 | 3
The other G17 v G16 p+ comparisons are similar:
GOES-16 systematically low by 2-3x
P1 out-of-family, high
GOES-17 vs GOES-16 Protons
Other telescopes exhibit similar behavior, as can be seen in the G17 provisional PS-PVR.

## Slide 49: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Results
Telescope Order, North-to-South |  | 
G15 MAG ED/PD | G17 MPS-HI E | G17 MPS-HI P
7 | 3 | 1
8 | 1 | 4
1 | 4 | 2
6 | 2 | 5
9 | 5 | 3
Compare fluxes from GOES-15 and GOES-17 when separated by 9.2 deg longitude
  28 March – 8 September 2019 (GOES-15 inverted, GOES-17 upright)
    After G17 reached GOES-West, while G15 continued operations
    Data limitations:
      Publicly-available data (G17 L2 data started in late Dec 2018 after Provisional status reached)
      G15 MAGE/PD turned off Nov 2018 – Jan 2019 due to high temperatures
      G15 MAGED turned off for good 8 Oct 2019
      Yaw flips at different times complicate comparisons
  Compare percentile fluxes between telescopes of same orientation
    0, ±35, ±70 deg from zenith (radially outward)
  This is the first time G15 data have been used in MPS-HI cal/val
New post-provisional comparison of GOES-15 and GOES-17

## Slide 50: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Results
Telescope Order, North-to-South |  | 
G15 MAG ED/PD | G17 MPS-HI E | G17 MPS-HI P
7 | 3 | 1
8 | 1 | 4
1 | 4 | 2
6 | 2 | 5
9 | 5 | 3
GOES-15 vs GOES-17 Electrons

## Slide 51: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Results
GOES-15 vs GOES-17 Electrons, 03/28/2019– 09/08/2019
RMS, 1-Q50(G15)/Q50(G17) = 0.238
By comparison,
RMS, 1-Q50(G13)/Q50(G16) = 0.216 (when separated by 15 deg)
= 0.198 (when separated by 0.7 deg)
[Boudouridis+ 2020]
The comparisons are made by taking the ratio of the GOES‐15 to the GOES‐17 percentile fluxes, following interpolation to five common energies (80, 130, 180, 270, and 380 keV) assuming a piecewise power‐law distribution.

## Slide 52: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Results
Telescope Order, North-to-South |  | 
G15 MAG ED/PD | G17 MPS-HI E | G17 MPS-HI P
7 | 3 | 1
8 | 1 | 4
1 | 4 | 2
6 | 2 | 5
9 | 5 | 3
GOES-15 vs GOES-17 Protons

## Slide 53: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Results
GOES-15 vs GOES-17 Protons, 03/28/2019– 09/08/2019
RMS, 1-Q50(G15)/Q50(G17) = 0.707
G13-15 MAGPD demonstrated to suffer radiation damage over time
[Rodriguez+ 2020, JSWSC, https://doi.org/10.1051/swsc/2020031]
The comparisons are made by taking the ratio of the GOES‐15 to the GOES‐17 percentile fluxes, following interpolation to five common energies (110, 130, 190, 270, and 410 keV) assuming a piecewise power‐law distribution.

## Slide 54: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Results
Comparison of >2 MeV electron fluxes: Use a rigorous method to compare two time series at different satellites : ‘Statistical Asynchronous Regression’ [O’Brien et al., JGR, 106, 2001]
GOES-16 vs GOES-13
GOES-17 vs GOES-14
GOES-17 vs GOES-16
Pre-Provisional results show good agreement between the various satellites in the operationally important range, flux > 1000 particles/(cm2 s sr)

## Slide 55: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Results
Post-Provisional study: GOES-15 vs GOES-17 >2 MeV Electrons, 03/28/2019– 09/08/2019
G15 E2W channel not shown due to degradation
[Baker+ 2019, JGR, https://doi.org/10.1029/2019JA027331]
10th and 25th percentiles are overcorrected (invalid) values
Asynchronous regression between
G17 T1 & T4 and G15 >2 MeV fluxes
75% percentile is just below 1000 1/cm2 s sr alert level
Good agreement between G15 and G17 around alert level

## Slide 56: PLPT-SEI-005: Cross-Satellite Comparison of Trapped Particles: Summary
Electrons:
  Good agreement between G16 & G17 MPS-HI incl. >2 MeV channel
    Exception: G16 Etel4 E3 spectra are out-of-family – presented challenges in ground cal due to large differences in actual thresholds from modeled
  Reasonable agreement between G17 MPS-HI and G14 MAGED
    MAGED a little low at lower energies
  Reasonable agreement between G17 T1 & T4 and G14 >2 MeV electrons
    Expect differences between EPEAD and MPS-HI due to different FOVs
    Difference between 2017 G16 vs. G13 comparisons and 2018 G17 vs. G14 comparisons is most likely due to the environment
Protons:
  G16 MPS-HI and G14 MAGPD are a factor of 2-3 low compared to G17 MPS-HI
  Degradation of the proton detectors? Discussion below
Partial pass

## Slide 57
MPS-HI E9-E11 Background Removal
The four highest-energy electron channels from MPS-HI (E9, E10, E10A, and E11) are susceptible to contamination by 100’s of MeV protons. The baseline correction algorithm (CDRL80F) uses fluxes from SGPS –X P9, P10 and P11 to estimate and remove the spurious rates due to proton contamination.
At launch CDRL80F sets , , .
Together with the values for E9, E10, and E10A, they comprise the dataset "theOutOfBandWeightingFactors" in the CALINR LUT for MPS-HI.
The baseline correction derives and for solar proton spectra from Geant4 simulations of the proton responses of the electron channels.
The baseline algorithm was inadequate to correct for the observed slowly-varying background due presumably to galactic cosmic ray (GCR) protons.
PLPT-SEI-006: Backgrounds
Pass

## Slide 58
MPS-HI E9-E11 Revised Background Removal
(GOES-16 ADR407, GOES-17 ADR762)
The background removal coefficients were corrected so as to better account for the GCR proton contamination (Juan Rodriguez, Pre-Provisional). This involves a number of observations and assumptions (demonstrated for MPS-HI E11):
SGPS-X channels P9, P10, and P11 suffer from a diurnal variation due to a sensitivity to a large daily temperature swing.
P11 has the smallest variation, and therefore is used exclusively for the background correction, , , .
The remaining coefficient is calculated separately for each telescope (the LUT can accommodate this).
The background level has changed very little during the first several months of the mission, therefore we can average the SGPS-X P11 fluxes and the background fluxes in E11 due to the GCRs, yielding
PLPT-SEI-006: Backgrounds

## Slide 59
Modeling the GCR background
Assume that the peak and the part of the PDF below the peak are dominated by the rates due to GCRs, model as Gaussians.
Gaussian PDF:
Gaussian CDF:
Fit the same part of the CDF, varying smoothly. Fitted parameters, , , . Reconstruct the PDF.
Do the same for SGPS-X P11 counts,
G16, 5-min averages, 01/09/2017-07/31/2017.
G17, 5-min averages, 04/24/2018-08/31/2018.
Apply at 1s L1b data.
PLPT-SEI-006: Backgrounds

## Slide 60
Gamma correction coefficient calculated for GOES-17 MPS-HI E9-E11, incorporated into revised MPS-HI LUT (ADR 762, October 15, 2018).
 | T1 | T2 | T3 | T4 | T5
E9 | 0.3641 | 0.3543 | 0.3724 | 0.4307 | 0.3776
E10 | 0.6369 | 0.6620 | 0.6693 | 0.7234 | 0.6686
E10a | 0.5829 | 0.5744 | 0.5707 | 0.5683 | 0.5084
E11 | 1.501 | 1.538 | 1.556 | 1.638 | 1.481
PLPT-SEI-006: Backgrounds
 | T1 | T2 | T3 | T4 | T5
E9 | 0.3782 | 0.4758 | 0.4155 | 0.2721 | 0.4513
E10 | 0.6490 | 0.5929 | 0.6052 | 0.5213 | 0.5538
E10a | 0.5446 | 0.2715 | 0.3842 | 0.5278 | 0.3977
E11 | 1.472 | 1.252 | 1.325 | 1.281 | 1.303
GOES-16/-17 LUT updates
Gamma correction coefficient calculated for GOES-16 MPS-HI E9-E11, incorporated into revised MPS-HI LUT (ADR 407, November 14, 2017).

## Slide 61
T2
T4
T1
T3
DOS
T5
GOES-16 E11 MeV)
SWPC alert level very close to uncorrected background
PLPT-SEI-006: Backgrounds

## Slide 62
T2
T4
T1
T3
DOS
T5
GOES-17 E11 MeV)
SWPC alert level very close to uncorrected background
PLPT-SEI-006: Backgrounds

## Slide 63: Product quality EVALUATION
GOES-16 and GOES-17 MPS-HI L1b Products Full PS-PVR

## Slide 64: GOES-16: Status at Full Review
 | Observed Issue | Root Cause | Future Outlook
Proton differential flux | Possible P1-P4 channel degradation Also present in P5-P7 Ratio of initial to final rates 3-10 | Dead layer forming on the detectors? Channel turn on energy shifts to higher energy with time | ATC SEA39 to test an MPS-HI unit in the Lab to replicate the degradation Linear fit correction of past fluxes (tested by MIT, can be implemented at NCEI), requires reprocessing of old data Compare with GOES-T after launch
Proton contamination of electron channels | SWPC is concerned it could be an issue during Solar Energetic Particle (SEP) events Can affect the operational E11 (>2 MeV) channel alerts | Energetic proton penetration of the electron detector shielding | Investigate correlation of electron fluxes with MPS-HI and SGPS proton fluxes Requires a strong SEP event, with low concurrent electron fluxes NCEI will continue monitoring
G16, G17 E11 fluxes | SWPC reported G17 E11 (> 2 MeV) fluxes higher than G16 at the end of August 2020 G17/G16 average flux ratios as high as 6-8 | Ratios <4.4 consistent with different spacecraft location, radiation environment Ratios >4.4 possible during active conditions | Resolved NCEI will continue monitoring
G16 P1 channel calibration | MIT reported G16 channel P1 out of family, higher than G17 P1 ATC believes performance is as expected | Inaccurate G16 P1 geometric factor (too low)? | Compare with channel P1 of GOES-T If needed, new beam calibration of another detector P1 channel
Solar proton channels | MPS-HI channels P9-P11 not in agreement with SGPS P2-P4 | Inaccurate geometric factors or energies | Calibration of later MPS-HI and SGPS T1 units at Brookhaven VdG

## Slide 65: GOES-17: Status at Full Review
 | Current Status | Root cause | Future Outlook
Proton differential flux | Possible P1-P4 channel degradation Also present in channels P5-P7 Ratio of initial to final rates 2-3 | Dead layer forming on the detectors? Channel turn on energy shifts to higher energy with time | ATC SEA39 to test an MPS-HI unit in the Lab to replicate the degradation Linear fit correction of past fluxes (tested by MIT, can be implemented at NCEI), requires reprocessing of old data Compare with GOES-T after launch
Proton contamination of electron channels | SWPC is concerned it could be an issue during Solar Energetic Particle (SEP) events Can affect the operational E11 (>2 MeV) channel alerts | Energetic proton penetration of the electron detector shielding | Investigate correlation of electron fluxes with MPS-HI and SGPS proton fluxes Requires a strong SEP event, with low concurrent electron fluxes NCEI will continue monitoring
G16, G17 E11 fluxes | SWPC reported G17 E11 (> 2 MeV) fluxes higher than G16 at the end of August 2020 G17/G16 average flux ratios as high as 6-8 | Ratios <4.4 consistent with different spacecraft location, radiation environment Ratios >4.4 possible during active conditions | Resolved NCEI will continue monitoring
Solar proton channels | Status not known due to lack of suitable SEP events for cross-comparison | N/A | Calibration of later MPS-HI and SGPS T1 units at Brookhaven VdG

## Slide 66
Proton Differential Flux
Apparent decline of low-energy channel proton rates by about an order of magnitude between January 2017 and July 2020

## Slide 67
Proton Differential Flux
Linear Least Squares Fitting of the daily average proton rates from January 2017 to December 2020 reveals a smaller trend, but present nevertheless
Ratios of initial over final rate based on the least squares fitting

## Slide 68
Proton Differential Flux
Linear Least Squares Fitting of the daily average proton rates from May 2018 to December 2020 reveals a smaller decline for GOES-17, only for P1-P5
Ratios of initial over final rate based on the least squares fitting

## Slide 69
Proton Differential Flux
ATC investigation (early 2021)
Extended NCEI original study into early 2021.
Oulu neutron monitor reveals a solar minimum in early 2020 (neutron flux maximizes at solar minimum), responsible for the MPS-HI prior flux decline.
Expected uptick in MPS-HI proton fluxes observed in early 2021.
ATC conclusion: MPS-HI observes normal space environment associated with the large scale solar cycle. No degradation in the MPS-HI proton detectors.
Credit ATC
Credit ATC
Solar Min
Uptick in 2021
Increasing activity

## Slide 70
Proton Differential Flux
Linear Least Squares Fitting of the daily average proton rates from January 2017 to September 2021 reveals a continuing decline
Ratios of initial over final rate based on the least squares fitting
Previous study limit, December 2020
Uptick observed by ATC
Further decline
3.39
4.40
5.28
5.51
5.01
4.12
3.97
Red values denote results of past study to December 2020
Results for other telescopes in backup slides

## Slide 71
Proton Differential Flux
Linear Least Squares Fitting of the daily average proton rates from May 2018 to September 2021 reveals a continuing decline
Ratios of initial over final rate based on the least squares fitting
Previous study limit, December 2020
Uptick observed by ATC
Further decline
1.56
1.89
2.19
2.07
1.53
0.96
0.56
Red values denote results of past study to December 2020
Results for other telescopes in backup slides

## Slide 72: MPS-HI electron telescope design greatly reduces contamination from SEP protons
GOES-13 EPEAD >2 MeV e- channel sensitive to >17 MeV p+
GOES-16 MPS-HI >2 MeV e- channel sensitive to >300 MeV p+
SEP flux correction is much smaller than on GOES-13
GOES-16 MPS-HI Dosimeter-2 LOLET channel (>1.2 MeV e-) is insensitive to MeV protons in these events
SEP contamination in E11 could not be observed due to elevated >2 MeV e- fluxes, small increase in >300 MeV p+ fluxes over GCR background
SEP contamination signal is comparable to total signal – inaccurate residuals
Overcorrection – false flux dropouts
Correction did not reveal true flux dropouts
GLE 72 onset
An uncontaminated E11 T4 channel would produce a similar time series
Proton Contamination
of Electron Channels
GOES-13 and GOES-16 observations (September 1-17, 2017)

## Slide 73
Proton Contamination
of Electron Channels
No electron response! Electron detector design successful in preventing proton contamination
Small SEP event observed by MPS-HI and SGPS protons, May 28-31, 2021
SGPS P7 40-80 MeV (yellow trace)
maximum energy channel to be enhanced by SEP
Similar results exist for other telescope look directions

## Slide 74
Proton Contamination
of Electron Channels
No electron response! Electron detector design successful in preventing proton contamination
Small SEP event observed by MPS-HI and SGPS protons, May 28-31, 2021
SGPS P7 40-80 MeV (yellow trace)
maximum energy channel to be enhanced by SEP
Similar results exist for other telescope look directions

## Slide 75
Factor of 3
Factor of 4
Factor of 5
Are the differences between G16 and G17 MPS-HI E11 (>2 MeV) channels attributable to physical, magnetospheric differences in flux at G16 and G17 locations?
GOES-16 and GOES-17 ETel4 E11 SWPC observations
GOES-16/-17 E11 fluxes
GOES-17 E11 higher than GOES-16 E11

## Slide 76: Meredith et al. (Space Weather, 2015), Extreme relativistic electron fluxes at geosynchronous orbit: Analysis of GOES E > 2 MeV electrons
Geographic
equator
Geomagnetic
equator
G17
G16
“…find that the daily averaged flux measured at GOES West is typically a factor of about 2.5 higher than that measured at GOES East”
“…due to the fact that GOES West and GOES East, which operate at 135o and 75oW, respectively, are located at different magnetic latitudes and hence at different L shells with GOES East typically being of the order of 0.2L farther from the Earth. Since the radial gradient of flux is generally outward near geosynchronous orbit, GOES West will typically measure larger fluxes than GOES East [Onsager et al., 2004]…”
G17
G16
Geomagnetic equator
L-shells
(dipole field lines)
GOES-16/-17 E11 fluxes

## Slide 77: Meredith et al. (Space Weather, 2015), Extreme relativistic electron fluxes at geosynchronous orbit: Analysis of GOES E > 2 MeV electrons
GOES-16/-17 E11 fluxes
West/East
flux ratios
2.6
2.8
4.4
4.0
2.8
2.8
2.8
2.6
2.9
2.9
GOES-West / GOES-East EPS flux ratios up to 4.4 in Meredith et al. (2015)

## Slide 78
GOES-16/-17 E11 fluxes
Plot GOES-16/-17 MPS-HI ETel4 E11 L0 hourly averaged counts for the same period as SWPC
Multiply GOES-16 E11 fluxes by 2.5 (Meredith et al. [2015])
Plot against Local Time to account for the spacecraft difference in longitude
Take the ratio GOES-17/GOES-16 of E11 hourly averaged counts
The two count rates, after GOES-16 is multiplied by 2.5, are similar
The G17/G16 ratio is below 2.5 whenever there are significant rates
Lower count rates
2.5
4.4

## Slide 79
GOES-16/-17 E11 fluxes
Plot GOES-16/-17 MPS-HI ETel4 E11 L2 daily averaged fluxes for the entire mission after the GOES-17 backgrounds were removed, October 2018 to August 2021
Multiply GOES-16 E11 fluxes by 2.5 (Meredith et al. [2015])
Plot against Local Time to account for the spacecraft difference in longitude
Take the ratio GOES-17/GOES-16 of E11 daily averaged fluxes
2.5
4.4
G17/G16 ratios are mostly in the expected range.
Some higher than expected ratios, usually for lower flux levels.
During periods of high geomagnetic activity, it is also possible that the ratio becomes even higher. For example, when the tail current moves inward, G16 experiences more losses than G17, being at higher L-shell

## Slide 80
GOES-16/-17 E11 fluxes
Make the histogram of GOES-16/-17 MPS-HI ETel4 E11 L2 daily averaged fluxes for the October 2018 to August 2021 period (previous plot)
The vast majority of G17/G16 ratios are in the expected range, 83.5% < 2.5, 98.4% < 4.4.
The differences between G16 and G17 MPS-HI E11 (>2 MeV) channels IS attributable to physical, magnetospheric differences in flux at G16 and G17 locations.

## Slide 81
GOES-16 P1 channel calibration
G16 P1 out-of-family with the other G16 channels
Higher than G17 P1 channel
Observed for all telescopes
GOES-17 vs GOES-16 Protons
P1
P2
P3
P4
P5
MIT Lincoln Labs submitted ADR 1155 in March 2021: G16 MPS-Hi P1 Channel Calibration Refinement
GOES-16 MPS-HI P1 channel fluxes are consistently high with respect to all the other channels and with the fluxes of GOES-17 MPS-Hi. LUT is consistent with GOES-16 CDRL079. The instrument vendor should re-evaluate the calibration data and propose a revision to the calibration values (energy band center and/or geometric factor) for the P1 channel.

## Slide 82
GOES-16 P1 channel calibration
P1
P2
P3
P4
P5
ATC compared G16 and G17 proton fluxes normalized to P3 channel flux, to LANL CPA fluxes normalized to fluxes at energy of 190 keV.
Found G16 P1 response higher than G17 but still within expected range as compared to LANL CPA.
Similar relations occur for other telescope pairs.
ATC conclusion: there is no need to re-evaluate the energy or geometric factor of G16 P1 channel.
Program has agreed to defer resolution of ADR 1155 to comparison with GOES-T MPS-HI proton data after launch.
ATC investigation (October 2021)
LANL data courtesy of Joe Borovsky
Plot credit ATC
LANL CPA data from 8 spacecraft and years 1976-1995 (Borovsky et al. [2016], JGRSP)
Daily averages

## Slide 83
Proton differential flux
  Possible proton channel degradation
  Continues to date
  Compare with GOES-T data after launch
Proton contamination of electron channels
  No electron channel contamination observed in recent SEP event
  Electron detector design successful
  Strong SEP event required for definitive answer (NCEI will continue monitoring)
G16, G17 E11 fluxes
  G17/G16 E11 ratios consistent with different spacecraft location, radiation environment
G16 P1 channel calibration
  G16 P1 channel reported out of family with the rest of the G16 proton channels, higher than G17 P1 channel
  Compare with GOES-T data after launch
Solar Proton channels
  MPS-HI channels P9-P11 not in agreement with SGPS P2-P4
  Requires beam calibration (has been agreed by the program, to be planned by ATC)
GOES-16: Status at Full Review
Summary

## Slide 84
Proton differential flux
  Possible proton channel degradation
  Continues to date
  Compare with GOES-T data after launch
Proton contamination of electron channels
  No electron channel contamination observed in recent SEP event
  Electron detector design successful
  Strong SEP event required for definitive answer (NCEI will continue monitoring)
G16, G17 E11 fluxes
  G17/G16 E11 ratios consistent with different spacecraft location, radiation environment
Solar Proton channels
  Status not known due to lack of suitable SEP events for cross-comparison
  Requires an SEP event during active geomagnetic conditions to achieve isotropic particle distribution
GOES-17: Status at Full Review
Summary

## Slide 85: Full Maturity Assessment
GOES-16 and GOES-17 MPS-HI L1b Products Full PS-PVR

## Slide 86: Full Validation
Preparation Activities | Assessment
Validation, quality assurance, and anomaly resolution activities are ongoing. | Validation activities are ongoing. Results have been discussed with SWPC.
Incremental product improvements may still be occurring. | Incremental product improvements are expected, primarily through updated LUTs incorporating results of cross-cal.
Users are engaged and user feedback is assessed. | Engagement with the operational and scientific community is on an ongoing basis. User concerns and questions are routinely addressed.
From 416-R-RIMP-0318 Version 1.1 07/22/2016,
Responsible Organization: GOES-R Ground Segment/Code 416

## Slide 87: Full Validation
End State | Assessment
Product performance for all products is defined and documented over a wide range of representative conditions via ongoing ground-truth and validation efforts. | PLPTs performed on reprocessed and/or L1b MPS-HI fluxes during various periods throughout the mission.
Products are operationally optimized, as necessary, considering mission parameters of cost, schedule, and technical competence as compared to user expectations. | Yes, to the limited extent of available resources and time, prioritized based on customer needs.
All known product anomalies are documented and shared with the user community. | This presentation, the L1b Readme files, the memos on background correction, and article by Boudouridis et al. [2020] in Space Weather.
Product is operational. | NCEI: yes. SWPC: yes.
From 416-R-RIMP-0318 Version 1.1 07/22/2016,
Responsible Organization: GOES-R Ground Segment/Code 416

## Slide 88
Performance Baseline Status
Assessment at Full Validation
MRD ID | Description | Related PLPTs | Status
1996 | MPS-HI Orthogonality/Coverage | -02, -04 | PLPTs completed
2000 | MPS-HI Measurement Range | -02, -04 | PLPTs completed
2001 | MPS-HI Measurement Accuracy | -02, -04, -05, -06 | PLPTs completed
MRD1996: Data in 5 directions
  Currently being met for electrons and protons
MRD2000: Measurement Range
  Requirements: Electrons 50 keV to 4 MeV plus >2 MeV; Protons 80 keV to 10 MeV
  Currently, all channels are functional and exhibit characteristic variation in behavior w/ energy
  Ground cal & cross-cal activities indicate that energy measurement range is covered
    G17 P8-P11 require SEP event suitable for cross comparisons with SGPS and G16 MPS-HI
MRD2001: Measurement Accuracy
  Requirements: @min flux <45%, @10X min flux < 25%
  Absolute accuracy cannot be verified on-orbit
  Results of PLPT-05 indicate that GOES-16 proton fluxes are systematically low by 2-3x relative to GOES-17
  Results of PLPT-02 indicate that the inter-telescope differences are much greater than 25% in many occasions, G16 proton/electrons, G17 protons
  Results of PLPT-04 shows that G16 MPS-HI P8-P11 reported fluxes are systematically low, with greater error in higher energy channels, up to >10x lower in P11

## Slide 89: Remaining Risks
Risk Name | Description | Impact | Mitigation and Schedule
MPS-HI solar proton channel disagreement | IF MPS-HI P8-P11 and SGPS P1-P5 are not both calibrated at BNL VdG | THEN root cause of large disagreement will not be understood | Program has authorized ATC to add MPS-HI calibration to planned effort at BNL VdG Wait for next SEP event to cross-cal G16 & G17
MPS-HI proton channel degradation | IF difference between G17 and G16 MPS-HI protons is due to on-orbit radiation damage | THEN all MPS-HI proton fluxes will be degraded starting 1-2 years after launch | Determine whether this is the root cause of discrepancy by comparison to GOES-T proton data Update LUTs or develop new metadata on effective energies

## Slide 90: Summary & Recommendations
GOES-16 and GOES-17 MPS-HI L1b Products Full PS-PVR

## Slide 91: Summary
ADR/WR status: most ADRs identified at Provisional have been closed or have clear path forward
  ADR 780: revisit, remedy has been identified and work is proceeding
  ADRs 863/872: on hold, deemed not critical for Full Maturity
    ADR 863 might not be critical for Full Maturity, but can become critical in case of catastrophic SGPS failure, as SWPC alert channel E11 will be lost
  ADR 1155: on hold until the launch of GOES-T
Planned Full PLPTs have been completed
  Except PLPT-SEI-004 Solar Energetic Particle (SEP) Cross-Comparison for G17 due to lack of suitable SEP events for cross-comparison since the G17 launch
Remaining risks have been identified
  Possible degradation of the MPS-HI proton channels: Wait for GOES-T
  MPS-HI and SGPS SEP channel disagreement: Beam Calibration is needed for MPS-HI P8-P11 channels

## Slide 92: Recommendations
NCEI believes that the GOES-16 MPS-HI L1b product has reached the Full Maturity as defined by the GOES-R Program
NCEI believes that the GOES-17 MPS-HI L1b product has reached the Full Maturity as defined by the GOES-R Program

## Slide 93: Backup slides
GOES-16 and GOES-17 MPS-HI L1b Products Full PS-PVR

## Slide 94: PLPT-SEI-004: SEP Channel Cross-Comparison: MPS-HI P9 and SGPS P2A/P2B during a period of high solar wind dynamic pressure (isotropic distribution)
Period with SW Pdyn > 10 nPa
MPS-HI P9 lower than SGPS+X/-X P2A, similar to SGPS+X/-X P2B.
(West)
(East)
At times of high solar wind dynamic pressure (Pdyn > 10 nPa), the “inside” and “outside” fluxes are approximately equal.
Rodriguez et al. (2010), The east‐west effect in solar proton flux measurements in geostationary orbit: A new GOES capability, Geophys. Res. Lett., Vol. 37, L07109, doi:10.1029/2010GL042531.
Discrepancies between the SGPS channels.
GOES-16

## Slide 95: PLPT-SEI-004: SEP Channel Cross-Comparison: MPS-HI P10 and SGPS P3 during a period of high solar wind dynamic pressure
Period with SW Pdyn > 10 nPa
MPS-HI P10 lower than SGPS+X/-X P3.
(West)
(East)
At times of high solar wind dynamic pressure (Pdyn > 10 nPa), the “inside” and “outside” fluxes are approximately equal.
Rodriguez et al. (2010), The east‐west effect in solar proton flux measurements in geostationary orbit: A new GOES capability, Geophys. Res. Lett., Vol. 37, L07109, doi:10.1029/2010GL042531.
GOES-16

## Slide 96
Proton Differential Flux
Future projection if the linear trend continues for 5 years, to December 2025
Ratios of initial over final rate, R1/R2, and future ratios, R1/R3, based on the least squares fitting
Proton channel degradation projection

## Slide 97
Proton Differential Flux
Future projection if the linear trend continues for 5 years, to December 2025
Ratios of initial over final rate, R1/R2, and future ratios, R1/R3, based on the least squares fitting
Proton channel degradation projection

## Slide 98
Proton Differential Flux
Proton channel degradation linear fits
(remaining telescopes)

## Slide 99
Proton Differential Flux
Linear Least Squares Fitting of the daily average proton rates from January 2017 to September 2021 reveals a continuing decline
Ratios of initial over final rate based on the least squares fitting
Previous study limit, December 2020
3.72
4.84
5.59
5.53
4.85
4.12
4.07
Red values denote results of past study to December 2020

## Slide 100
Proton Differential Flux
Linear Least Squares Fitting of the daily average proton rates from January 2017 to September 2021 reveals a continuing decline
Ratios of initial over final rate based on the least squares fitting
Previous study limit, December 2020
4.31
5.53
6.56
6.84
6.54
5.87
6.35
Red values denote results of past study to December 2020

## Slide 101
Proton Differential Flux
Linear Least Squares Fitting of the daily average proton rates from January 2017 to September 2021 reveals a continuing decline
Ratios of initial over final rate based on the least squares fitting
Previous study limit, December 2020
4.39
5.98
7.43
8.03
7.81
7.43
8.15
Red values denote results of past study to December 2020

## Slide 102
Proton Differential Flux
Linear Least Squares Fitting of the daily average proton rates from January 2017 to September 2021 reveals a continuing decline
Ratios of initial over final rate based on the least squares fitting
Previous study limit, December 2020
5.90
7.32
8.28
8.60
8.67
9.00
9.85
Red values denote results of past study to December 2020

## Slide 103
Proton Differential Flux
Linear Least Squares Fitting of the daily average proton rates from May 2018 to September 2021 reveals a continuing decline
Ratios of initial over final rate based on the least squares fitting
Previous study limit, December 2020
1.54
1.65
1.78
1.73
1.43
1.10
0.88
Red values denote results of past study to December 2020

## Slide 104
Proton Differential Flux
Linear Least Squares Fitting of the daily average proton rates from May 2018 to September 2021 reveals a continuing decline
Ratios of initial over final rate based on the least squares fitting
Previous study limit, December 2020
1.28
1.44
1.58
1.45
1.09
0.73
0.58
Red values denote results of past study to December 2020

## Slide 105
Proton Differential Flux
Linear Least Squares Fitting of the daily average proton rates from May 2018 to September 2021 reveals a continuing decline
Ratios of initial over final rate based on the least squares fitting
Previous study limit, December 2020
1.86
1.93
2.00
1.86
1.58
1.36
1.25
Red values denote results of past study to December 2020

## Slide 106
Proton Differential Flux
Linear Least Squares Fitting of the daily average proton rates from May 2018 to September 2021 reveals a continuing decline
Ratios of initial over final rate based on the least squares fitting
Previous study limit, December 2020
2.09
2.08
2.07
1.90
1.62
1.39
1.31
Red values denote results of past study to December 2020