## Slide 1: GOES-16/18 Fractional Snow Cover L2 Provisional Validation Peer/Stakeholder Product Validation Review (PS-PVR) Dec. 9, 2022 (slides revised Dec. 15, 2022) AWIPS Verification / NWS Perspective John D. Evans and Derek van Pelt TOWR-S team, NWS Office of Observations

## Slide 2: GOES-16 (GOES-East) Fractional Snow Cover in AWIPS
GOES-16 Full Disk Fractional Snow Cover Dec. 12, 2022 (13:20-18:30z)

## Slide 3: GOES-16 (GOES-East) Fractional Snow Cover in AWIPS
GOES-16 Full Disk Fractional Snow Cover Dec. 12, 2022 (19:00-21:10z)

## Slide 4: GOES-18 Fractional Snow Cover in AWIPS
GOES-18 Full Disk Fractional Snow Cover Dec. 12, 2022 (13:20-21:10z)

## Slide 5: Notes on Fractional Snow Cover (FSC) & AWIPS
AWIPS can ingest the Enterprise FSC product… However the baseline configuration for legacy FSC doesn’t produce a useful display with Enterprise FSC 🠞
(Parameter “FSC” has been redefined; also “DQF”)
The configuration updates (new FSC units specification, DQF masking rule, and new color table) will be deployed through the TOWR-S RPM process.
  No AWIPS code changes required
1-minute (Meso) and 5-minute (CONUS) revisits of FSC are probably overkill for most users; but they might be intermediate products used in building cloud-cleared composite views of FSC every 30 or 60 minutes.