## Slide 1
GOES-19 ABI L2+ LAP Products Provisional PS-PVR
February 5, 2025
Jaime Daniels, Mark Kulie
GOES-R AWG
NOAA/NESDIS/STAR
GOES-R AWG LAP team: Zhenglong Li, Pei Wang, Jinlong Li, Richard Dworak, Bill Bellon, UW-CIMSS

## Slide 2: Agenda
Provisional Validation Product Maturity Assessment
  Data since November 01, 2024
Path to Full Maturity Review
Summary and Recommendations

## Slide 3: Products Overview
Same as GOES-16, GOES-17, and GOES-18 ABI L2 LAP algorithm includes regression and physical retrieval based on the infrared spectral bands as input. The algorithm is applied to 5x5 ABI pixels (~10 km) for generating LAP products over clear sky. The LAP products include LVT, LVM, TPW, and DSI.
Band Number | Wavelength (µm) | Purpose
8 | 6.19 | High-level atmospheric water vapor, winds, rainfall
9 | 6.93 | Mid-level atmospheric water vapor, winds, rainfall
10 | 7.34 | Lower-level atmospheric water vapor, winds, and SO2
12 | 9.61* | Total ozone
13 | 10.33 | Surface and cloud
14 | 11.20 | Imagery, SST, clouds, rainfall
15 | 12.30 | Total water, ash, SST
16 | 13.30 | Air temperature, cloud heights and amounts
LAP products
Legacy Vertical Temperature profile (LVT)
Legacy Vertical Moisture profile (LVM)
Total Precipitable Water (TPW)
Derived Stability Indices (DSI)
              Lifted Index (LI)
              Convective Available Potential Energy (CAPE)
              Showalter Index (SI)
              K-Index (KI)
              Total Totals (TT)
9.61* : used only in regression
Notes: * Only used in the regression step.

## Slide 4: Review: Time-Line/Context
25 June 2024 GOES-U Launch
7 July 2024 GEO orbit attained (became GOES-19)
18 July 2024 GOES-19 arrived at its checkout location of 89.5W
24 July 2024 Post Launch Product Test (PLPT) begins
1 Oct 2024 Beta maturity achieved

## Slide 5: PLPTs Under Review
PLPT ID | Descriptive Title | % Complete | Results | AWG POC
ABI-FD_TPW06 | Quantitative analysis of M6 FD TPW | 100 | Complete | AWG
ABI-CONUS_TPW07 | Quantitative analysis of M6 CONUS TPW | 100 | Complete | AWG
ABI-MESO_TPW08 | Quantitative analysis of M6 Meso TPW | 100 | Complete | AWG
Notes: PRO is responsible for 01 – 05.

## Slide 6: PLPTs Under Review
PLPT ID | Descriptive Title | % Complete | Results | AWG POC
ABI-FD_LVT06 | Quantitative analysis of M6 FD LVT | 100 | Complete | AWG
ABI-CONUS_LVT07 | Quantitative analysis of M6 CONUS LVT | 100 | Complete | AWG
ABI-MESO_LVT08 | Quantitative analysis of M6 Meso LVT | 100 | Complete | AWG
Notes: PRO is responsible for 01 – 05.

## Slide 7: PLPTs Under Review
PLPT ID | Descriptive Title | % Complete | Results | AWG POC
ABI-FD_LVM06 | Quantitative analysis of M6 FD LVM | 100 | Complete | AWG
ABI-CONUS_LVM07 | Quantitative analysis of M6 CONUS LVM | 100 | Complete | AWG
ABI-MESO_LVM08 | Quantitative analysis of M6 Meso LVM | 100 | Complete | AWG
Notes: PRO is responsible for 01 – 05.

## Slide 8: PLPTs Under Review
PLPT ID | Descriptive Title | % Complete | Results | AWG POC
ABI-FD_DSI06 | Quantitative analysis of M6 FD DSI | 100 | Complete | AWG
ABI-CONUS_DSI07 | Quantitative analysis of M6 CONUS DSI | 100 | Complete | AWG
ABI-MESO_DSI08 | Quantitative analysis of M6 Meso DSI | 100 | Complete | AWG
Notes: PRO is responsible for 01 – 05.

## Slide 9: PLPT Tests for each Domain
Analysis Method | FD | CONUS | MESO
Visual Inspection |  |  | 
Comparison to reference data (RAOB and AMSR2) |  |  | 
Intercomparison to GOES-16 and 18 |  | N/A | N/A
Our 3 PLPTs dealing with analysis are comprised of the same 3 methods.
Each contains the applications of these methods on the FD, CONUS and MESO domains.
The applications of each method to each domain is summarized below.
Some methods were redundant or not possible for some domains.
Same as what was done for GOES-16/17/18 LAP

## Slide 10: Provisional Validation Product Maturity Assessment
GOES-19 ABI L2+ LAP Products Provisional PS-PVR

## Slide 11: GOES-19 Data Used in this Review
November 1, 2024, 1900 UTC:
  -Visual images of all domains for each variable
November and December 2024
  -All FD, CONUS, Meso1, and Meso2 LAP with RAOB TPW, DSI, and T/Q profile matchups within +/- 30 min, 20 km
November and December 2024
  -All FD, CONUS, Meso1, and Meso2 LAP with AMSR2 TPW matchups within +/- 30 min, 20 km
November 15, 2024, 0000 UTC:
  -GOES-19 and GOES-16 intercomparison
November 15, 2024, 0000 UTC:
  -GOES-19 and GOES-18 intercomparison
November 15, 2024, 0120 UTC – 0310 UTC:
  -Sun migration effect on product
11

## Slide 12: Definitions of Metrics
Passed: No visual artifacts and/or the comparison with the reference data near or above the specification.
Failed: Cause of performance degradation is unknown.
The comparisons with the reference data are computed over all data.
12

## Slide 13
Real-time GOES-19 ABI LAP product validation webpage soundingval.ssec.wisc.edu
Imagery (Fulldisk TPW)
Regional TPW Plots with AMRS-2
Station TPW Plots

## Slide 14: Examples of Visual Inspection of All Domains
14

## Slide 15: PLPT ABI-FD-TPW, LVT, LVM:
TPW (mm)
Temp (K). 500 hPa
WV (g/kg) 850 hPa
15
TPW: Total Precipitable Water
LVT: Legacy Vertical Temperature profile
LVM: Legacy Vertical Moisture profile
November 01 2024, 1900 UTC

## Slide 16: PLPT ABI-FD-DSI:
LI
CAPE
TT
KI
SI
16
LI: Lifted Index
CAPE: Convective Available Potential Energy
TT: Total Totals
KI: K-Index
SI: Showalter Index
November 01 2024, 1900 UTC

## Slide 17: PLPT ABI-CONUS-TPW, LVT, LVM:
TPW (mm)
Temp (K). 500 hPa
WV (g/kg) 850 hPa
17
TPW: Total Precipitable Water
LVT: Legacy Vertical Temperature profile
LVM: Legacy Vertical Moisture profile
November 01 2024, 1901 UTC

## Slide 18: PLPT ABI-CONUS-DSI:
LI
CAPE
TT
KI
SI
18
LI: Lifted Index
CAPE: Convective Available Potential Energy
TT: Total Totals
KI: K-Index
SI: Showalter Index
November 01 2024, 1901 UTC

## Slide 19: Comparison of TPW with the RAOB, AMSR2
19

## Slide 20: Requirements for ABI LAP product: TPW
20
Product |  | Accuracy | Precision | Range
Temperature |  | 1 K below 400 hPa and above boundary layer | 2 K below 400 hPa and above boundary layer | 180 - 320 K
Moisture |  | Sfc - 300 hPa: 18% 300 - 100 hPa: 20% | Sfc - 300 hPa: 18% 300 - 100 hPa: 20% | 0 - 100%
TPW |  | 1 mm | 3 mm | 0 - 100 mm
DSI | LI | 2.0 K | 6.5 K | -10 ~ 40 K or above
 | CAPE | 1000 J/kg | 2500 J/kg | 0 - 5000 J/kg
 | SI | 2.0 K | 6.5 K | -10 ~ 4 K or above
 | TT | 1 K | 4 K | -43 ~ 56 K
 | KI | 2 K | 6.5 K | 0 - 40 K

## Slide 21: PLPT ABI-FD-TPW vs RAOB:
2024. 11 ~ 2024. 12
21
Accuracy spec: 1 mm
Precision spec: 3 mm
number: 2364
bias: -0.26 mm
std: 2.12 mm
number: 2704
bias: -0.21 mm
std: 2.05 mm
PASSED

## Slide 22: PLPT ABI-CONUS-TPW vs RAOB:
2024. 11 ~ 2024. 12
22
Accuracy spec: 1 mm
Precision spec: 3 mm
number: 2041
bias: -0.20 mm
std: 1.87 mm
number: 2230
bias: -0.12 mm
std: 1.75 mm
PASSED

## Slide 23: PLPT ABI-FD-TPW vs AMSR2:
23
Accuracy spec: 1 mm
Precision spec: 3 mm
number: 395850
bias: -1.73 mm
std: 2.12 mm
2024. 11 ~ 2024. 12
number: 401770
bias: -1.49 mm
std: 2.05 mm
Large negative biases likely due to wet bias of AMSR2 in 202411 and 202412
Similar large negative biases from GOES-16 and 18
No such degradation from previous months from GOES-16/18
No such degradation from the comparisons with RAOB from GOES-16/18/19
PASSED

## Slide 24: PLPT ABI-CONUS-TPW vs AMSR2:
24
Accuracy spec: 1 mm
Precision spec: 3 mm
number: 43677
bias: -2.18 mm
std: 2.31 mm
2024. 11 ~ 2024. 12
number: 42292
bias: -1.82 mm
std: 2.06 mm
PASSED
Large negative biases likely due to wet bias of AMSR2 in 202411 and 202412
Similar large negative biases from GOES-16 and 18
No such degradation from previous months from GOES-16/18
No such degradation from the comparisons with RAOB from GOES-16/18/19

## Slide 25: TPW Performance Summary
TPW retrieval is working as expected on GOES-19 ABI data when combined with NWP short-range forecasts (as first guess);
With a quantitative web-based tool (http://soundingval.ssec.wisc.edu) and the comparisons with RAOB overall it does indicate performances meet spec. for all the coverages (FD, CONUS, Meso1, and Meso2),
The bias of the comparisons with AMSR-2 is a little comparatively large, likely due to wet bias from AMSR-2

## Slide 26: Comparison of LVT & LVM with the RAOB
26

## Slide 27: Requirements for ABI LAP products: LVT, LVM
27
Product |  | Accuracy | Precision | Range
Temperature (LVT) |  | 1 K below 400 hPa and above boundary layer | 2 K below 400 hPa and above boundary layer | 180 - 320 K
Moisture (LVM) |  | Sfc - 300 hPa: 18% 300 - 100 hPa: 20% | Sfc - 300 hPa: 18% 300 - 100 hPa: 20% | 0 - 100%
TPW |  | 1 mm | 3 mm | 0 - 100 mm
DSI | LI | 2.0 K | 6.5 K | -10 ~ 40 K or above
 | CAPE | 1000 J/kg | 2500 J/kg | 0 - 5000 J/kg
 | SI | 2.0 K | 6.5 K | -10 ~ 4 K or above
 | TT | 1 K | 4 K | -43 ~ 56 K
 | KI | 2 K | 6.5 K | 0 - 40 K

## Slide 28: PLPT ABI-LVT, LVM (vs RAOB):
November 2024
28
LVT (K)
Accuracy spec:
1 K (BL-400hPa)
Precision spec:
2 K (BL-400hPa)
Full Disk Temp BIAS
Full Disk Temp STD
CONUS Temp BIAS
CONUS Temp STD
PASSED
Notes: Full disk has large STD possibly due to lower RAOB quality from non-USA countries. MESO might not have enough samples for statistics.

## Slide 29: PLPT ABI-LVT, LVM (vs RAOB):
November 2024
29
LVT (K)
Accuracy spec:
1 K (BL-400hPa)
Precision spec:
2 K (BL-400hPa)
MESO1 Temp BIAS
MESO1 Temp STD
MESO2 Temp BIAS
MESO2 Temp STD
PASSED
Notes: Full disk has large STD possibly due to lower RAOB quality from non-USA countries. MESO might not have enough samples for statistics.

## Slide 30: PLPT ABI-LVT, LVM (vs RAOB):
December 2024
30
LVT (K)
Accuracy spec:
1 K (BL-400hPa)
Precision spec:
2 K (BL-400hPa)
Full Disk Temp BIAS
Full Disk Temp STD
CONUS Temp BIAS
CONUS Temp STD
PASSED
Notes: Full disk has large STD possibly due to lower RAOB quality from non-USA countries. MESO might not have enough samples for statistics.

## Slide 31: PLPT ABI-LVT, LVM (vs RAOB):
December 2024
31
LVT (K)
Accuracy spec:
1 K (BL-400hPa)
Precision spec:
2 K (BL-400hPa)
MESO1 Temp BIAS
MESO1 Temp STD
MESO2 Temp BIAS
MESO2 Temp STD
PASSED
Notes: Full disk has large STD possibly due to lower RAOB quality from non-USA countries. MESO might not have enough samples for statistics.

## Slide 32: PLPT ABI-LVT, LVM (vs RAOB):
November 2024
32
Full Disk RH BIAS
Full Disk RH STD
CONUS RH BIAS
CONUS RH STD
LVM (%)
Accuracy & Precision spec:
18% (sfc-300hPa), 20% (300-100hPa)
Dry bias of RAOB in upper troposphere
limited moisture information in PBL and above 300hPa
PASSED
Notes: Full disk has large STD possibly due to lower RAOB quality from non-USA countries. MESO might not have enough samples for statistics.

## Slide 33: PLPT ABI-LVT, LVM (vs RAOB):
November 2024
33
MESO1 RH BIAS
MESO1 RH STD
MESO2 RH BIAS
MESO2 RH STD
LVM (%)
Accuracy & Precision spec:
18% (sfc-300hPa), 20% (300-100hPa)
PASSED
Dry bias of RAOB in upper troposphere
limited moisture information in PBL and above 300hPa
Notes: Full disk has large STD possibly due to lower RAOB quality from non-USA countries. MESO might not have enough samples for statistics.

## Slide 34: PLPT ABI-LVT, LVM (vs RAOB):
December 2024
34
Full Disk RH BIAS
Full Disk RH STD
CONUS RH BIAS
CONUS RH STD
LVM (%)
Accuracy & Precision spec:
18% (sfc-300hPa), 20% (300-100hPa)
Dry bias of RAOB in upper troposphere
limited moisture information in PBL and above 300hPa
PASSED
Notes: Full disk has large STD possibly due to lower RAOB quality from non-USA countries. MESO might not have enough samples for statistics.

## Slide 35: PLPT ABI-LVT, LVM (vs RAOB):
December 2024
35
MESO1 RH BIAS
MESO1 RH STD
MESO2 RH BIAS
MESO2 RH STD
LVM (%)
Accuracy & Precision spec:
18% (sfc-300hPa), 20% (300-100hPa)
PASSED
Dry bias of RAOB in upper troposphere
limited moisture information in PBL and above 300hPa
Notes: Full disk has large STD possibly due to lower RAOB quality from non-USA countries. MESO might not have enough samples for statistics.

## Slide 36: LVT and LVM Performance Summary
LVT and LVM retrievals are working as expected on GOES-19 ABI data when combined with NWP short-range forecasts (as first guess);
Retrievals are sensitive to first guess;
With a highly quantitative web-based tool (http://soundingval.ssec.wisc.edu) and the comparisons with RAOB, the performances overall meet spec. for all the coverages (FD, CONUS, Meso1, Meso2), except for the near surface temperature, and also for the Relative Humidity at upper troposphere (100 - 300 hPa) when compared with RAOB, which is likely due to the known issue of dry bias of radiosonde observations, possible lower quality from non-US RAOB, and reduced information content.
36

## Slide 37: Comparison of DSI with the RAOB
37

## Slide 38: Requirements for ABI LAP products: DSI
38
Product |  | Accuracy | Precision | Range
Temperature |  | 1 K below 400 hPa and above boundary layer | 2 K below 400 hPa and above boundary layer | 180 - 320 K
Moisture |  | Sfc - 300 hPa: 18% 300 - 100 hPa: 20% | Sfc - 300 hPa: 18% 300 - 100 hPa: 20% | 0 - 100%
TPW |  | 1 mm | 3 mm | 0 - 100 mm
DSI | LI | 2.0 K | 6.5 K | -10 ~ 40 K or above
 | CAPE | 1000 J/kg | 2500 J/kg | 0 - 5000 J/kg
 | SI | 2.0 K | 6.5 K | -10 ~ 4 K or above
 | TT | 1 K | 4 K | -43 ~ 56 K
 | KI | 2 K | 6.5 K | 0 - 40 K

## Slide 39: PLPT ABI-FD-DSI:
2024.11-2024.12
LI vs RAOB
39
Accuracy spec: 2 K
Precision spec: 6.5 K
number: 2001
bias: -0.53 K
std: 1.53 K
number: 2339
bias: -0.67 K
std: 1.76 K
PASSED
LI
LI

## Slide 40: PLPT ABI-FD-DSI:
2024.11-2024.12
CAPE vs RAOB
40
number: 542
bias: -147.77 J/kg
std: 277.47 J/kg
number: 483
bias: -109.42 J/kg
std: 267.64 J/kg
PASSED
CAPE
CAPE
Accuracy spec: 1000 J/kg
Precision spec: 2500 J/kg

## Slide 41: PLPT ABI-FD-DSI:
2024.11-2024.12
SI vs RAOB
41
Accuracy spec: 2 K
Precision spec: 6.5 K
PASSED
number: 2213
bias: -0.46 K
std: 2.74 K
number: 2128
bias: -0.75 K
std: 2.63 K
SI
SI

## Slide 42: PLPT ABI-FD-DSI:
2024.11-2024.12
KI vs RAOB
42
number: 989
bias: -0.88 K
std: 5.54 K
number: 956
bias: 0.09 K
std: 5.62 K
KI
KI
Accuracy spec: 2 K
Precision spec: 6.5 K
PASSED

## Slide 43: PLPT ABI-FD-DSI:
2024.11-2024.12
KI vs RAOB (KI>20)
43
number: 653
bias: -1.33 K
std: 3.82 K
KI
Accuracy spec: 2 K
Precision spec: 6.5 K
PASSED
K-Index | Thunderstorm Probability
Less than 20 | None
20-25 | Isolated Thunderstorms
26-30 | Widely Scattered Thunderstorms
31-35 | Scattered Thunderstorms
Above 35 | Numerous Thunderstorms

## Slide 44: PLPT ABI-FD-DSI:
2024.11-2024.12
TT vs RAOB
44
number: 2213
bias: 0.84 K
std: 5.51 K
number: 2135
bias: 0.61 K
std: 4.94 K
TT
TT
Accuracy spec: 1 K
Precision spec: 4 K

## Slide 45: PLPT ABI-FD-DSI:
2024.11-2024.12
TT vs RAOB (TT>20)
45
number: 3505
bias: -0.41 K
std: 3.42 K
TT
TT | Thunderstorm Probability
45-50 | Thunderstorms possible
50-55 | Thunderstorms more likely, possibly server
55-60 | Severe thunderstorms most likely
PASSED
Accuracy spec: 1 K
Precision spec: 4 K

## Slide 46: PLPT ABI-CONUS-DSI:
2024.11-2024.12
LI vs RAOB
46
Accuracy spec: 2 K
Precision spec: 6.5 K
number: 1717
bias: -0.41 K
std: 1.52 K
number: 1921
bias: -0.44 K
std: 1.59 K
PASSED
LI
LI

## Slide 47: PLPT ABI-CONUS-DSI:
2024.11-2024.12
CAPE vs RAOB
47
number: 341
bias: -161.56 J/kg
std: 310.00 J/kg
number: 282
bias: -118.73 J/kg
std: 323.00 J/kg
PASSED
CAPE
CAPE
Accuracy spec: 1000 J/kg
Precision spec: 2500 J/kg

## Slide 48: PLPT ABI-CONUS-DSI:
2024.11-2024.12
SI vs RAOB
48
Accuracy spec: 2 K
Precision spec: 6.5 K
PASSED
number: 1877
bias: -0.60 K
std: 2.76 K
number: 1711
bias: -1.04 K
std: 2.54 K
SI
SI

## Slide 49: PLPT ABI-CONUS-DSI:
2024.11-2024.12
KI vs RAOB
49
number: 706
bias: -0.68 K
std: 5.51 K
number: 666
bias: 0.04 K
std: 5.12 K
KI
KI
Accuracy spec: 2 K
Precision spec: 6.5 K
PASSED

## Slide 50: PLPT ABI-CONUS-DSI:
2024.11-2024.12
KI vs RAOB (KI>20)
50
number: 360
bias: -1.12 K
std: 3.67 K
KI
Accuracy spec: 2 K
Precision spec: 6.5 K
K-Index | Thunderstorm Probability
Less than 20 | None
20-25 | Isolated Thunderstorms
26-30 | Widely Scattered Thunderstorms
31-35 | Scattered Thunderstorms
Above 35 | Numerous Thunderstorms
PASSED

## Slide 51: PLPT ABI-CONUS-DSI:
2024.11-2024.12
TT vs RAOB
51
number: 1877
bias: 1.15 K
std: 5.49 K
number: 1718
bias: 0.83 K
std: 5.20 K
TT
TT
Accuracy spec: 1 K
Precision spec: 4 K

## Slide 52: PLPT ABI-CONUS-DSI:
2024.11-2024.12
TT vs RAOB (TT>20)
52
number: 2766
bias: -0.26 K
std: 3.48 K
TT
TT | Thunderstorm Probability
45-50 | Thunderstorms possible
50-55 | Thunderstorms more likely, possibly server
55-60 | Severe thunderstorms most likely
PASSED
Accuracy spec: 1 K
Precision spec: 4 K

## Slide 53: PLPT ABI-MESO1-DSI:
2024.11-2024.12
53
Accuracy spec: 2 K
Precision spec: 6.5 K
number: 190
bias: -0.50 K
std: 1.48 K
PASSED
LI
LI vs RAOB
CAPE
CAPE vs RAOB
Accuracy spec: 1000 J/kg
Precision spec: 2500 J/kg
number: 18
bias: -19.73 J/kg
std: 174.61 J/kg
PASSED

## Slide 54: PLPT ABI-MESO1-DSI:
2024.11-2024.12
54
Accuracy spec: 2 K
Precision spec: 6.5 K
number: 183
bias: -1.60 K
std: 2.30 K
PASSED
SI
SI vs RAOB
KI
KI vs RAOB
number: 47
bias: 0.39 K
std: 4.38 K
PASSED
Accuracy spec: 2 K
Precision spec: 6.5 K

## Slide 55: PLPT ABI-MESO1-DSI:
2024.11-2024.12
55
PASSED
TT
TT vs RAOB
TT
TT vs RAOB (TT>20 K)
number: 112
bias: 0.06 K
std: 3.13 K
Accuracy spec: 1 K
Precision spec: 4 K
number: 183
bias: 2.23 K
std: 6.79 K

## Slide 56: DSI Performance Summary
DSI retrieval is working as expected on GOES-19 ABI data when combined with NWP short-range forecasts (as first guess);
With a highly quantitative web-based tool (http://soundingval.ssec.wisc.edu) and the comparisons with RAOB, it indicates the performances from LI, CAPE and SI meet spec. for all the coverages
The comparisons of TT with RAOBs show the precisions are larger than specs. However, for unstable atmosphere, the precisions meet the requirement.
56

## Slide 57: GOES-16 vs. GOES-19 ABI LAP Products comparisons
Clear-sky, Overlapped coverage
GOES 16
GOES 19
GOES 16 – GOES 19
Temp at 500 mb
2024.11.15 00Z

## Slide 58
GOES-19 vs. GOES-16 comparisons
LVT and LVM
Statistical and STD for the overlapped area (zenith angle ≤ 65)
N = 133,237
N = 133,237
2024.11.15 00Z

## Slide 59
GOES-19 vs. GOES-16 comparisons
TPW and DSI
2024.11.15 00Z
G16 – G19 statistics (zenith angle ≤ 65)
SI
KI
TT
CAPE
TPW
LI

## Slide 60: GOES-18 vs. GOES-19 ABI LAP Products comparisons
Clear-sky, Overlapped coverage
GOES 18
GOES 19
GOES 18 – GOES 19
Temp at 500 mb
2024.11.15 00Z

## Slide 61
GOES-19 vs. GOES-18 comparisons
LVT and LVM
Statistical and STD for the overlapped area (zenith angle ≤ 65)
N = 133,237
N = 133,237
2024.11.15 00Z

## Slide 62
GOES-19 vs. GOES-18 comparisons
TPW and DSI
2024.11.15 00Z
G18 – G19 statistics (zenith angle ≤ 65)
SI
KI
TT
CAPE
TPW
LI

## Slide 63: PLPT Outcomes: Summary
All PLPT activities needed to make LAP products provisional have been completed.
Minor issues revealed by PLPTs:
-- Missing values in random areas
  Slightly large discrepancies of some DSI products (precisions of TT) compared with RAOB, but meeting the requirements for unstable atmosphere
These minor issues may not prevent the declaration of Provisional Maturity

## Slide 64: Path to Full Maturity Review

## Slide 65: Path to Full Maturity Review
We expect to apply the same PLPTs to be conducted for Full Maturity
  Extend period for testing throughout 2025.
  Save L2 to enable further comparisons with the reference datasets.
  Monitor the performance in warm seasons.
Currently minor issues may not prevent declaration of Full Maturity (5 issues identified through the PLPT work and will be mitigated during provisional stage)
  Missing values are randomly discovered over some areas.
  LAP products are affected by the migration of the sun which is likely caused by the cloud mask.
  TT values have slightly larger discrepancies when compared with (“point-source”) RAOBs; when considering only unstable atmospheric conditions, the results pass the requirement.
  Large wet bias when compared with RAOB around 200 hPa, likely due to the commonly known dry bias in RAOB
  Large moisture std when compared with RAOB around 200 hPa, likely due to the lack of sounding information content from ABI in upper troposphere

## Slide 66: Issue #1 – Missing data over random areas
Initial analysis showed missing data over random area
  The missing data occur occasionally and randomly in boxed shapes
Need to revisit ADR 956 on this issue
  The same issue still found for GOES-16, 18, and 19
  Reported to Rico
Notes: PRO team may clarify more about this.

## Slide 67: An example of the missing data

## Slide 68: Issue #2 – The effects of sun migration on products
Appears to be affecting large zenith angles more significantly
Notes: PRO team may clarify more about this.

## Slide 69: Risks to Reaching Full
Risk Name | Description | Impact | Mitigation and Schedule
Missing values over randomly distributed areas | Occasionally, there are missing values over randomly distributed boxed areas, in both the full disk and CONUS sectors. | Minor | Suggest an ADR, similar to an earlier one which we thought resolved.
The migration of the sun affecting the LAP products | The ABI LAP products are affected by sun-rise and sun-set. | Minor | Cloud mask may have influences on the ABI LAP products, as the scenes are illuminated, although appears to be a yield issue.
Wet bias of the relative humidity in upper troposphere (100 - 300 hPa) | The relative humidity in upper troposphere (100-300 hPa) shows large wet bias than the spec. | Minor | Radiosonde has dry bias in observing the relative humidity in the upper troposphere.
Moisture std of the relative humidity in upper troposphere (100 - 300 hPa) | The relative humidity in upper troposphere (100-300 hPa) shows large std than the spec. | Minor | Lack of information content in upper troposphere.
Slightly large discrepancy of several DSI | Several DSI show slightly larger discrepancy than the spec, compared to radiosondes. | Minor | If the atmospheric conditions are unstable, the statistics meet the requirements. May need a high spectrally resolution sounder in geo to fully resolve.
Small Impact
Moderate Impact
Large Impact

## Slide 70: SUMMARY AND RECOMMENDATIONS
GOES-19 ABI L2 LAP Product Provisional PS-PVR

## Slide 71: Summary
AWG LAP team has validated GOES-19 LAP products (TPW, LVT, LVM, DSI) from November 2024 to December 2024 with reference data from RAOB and AMSR2 in near real-time, the performance overall meet the requirements;
The intercomparisons between GOES-19 and GOES-16/18 show consistent results among LAP products from the three satellites;
AWG LAP team recommend that TPW, LVT, LVM, and DSI products be transitioned to Provisional status at this time;
AWG LAP team have found the following minor issues which should not prevent Provisional status
  Missing values occur occasionally and randomly over boxed areas.
  The migration of the sun affects the LAP products via cloud mask.
  Comparisons of TT with RAOBs shows a little larger than spec; when considering only unstable atmospheric conditions, the results pass the requirement.
  Comparisons of LVM with RAOBs shows larger wet bias than spec. in upper troposphere; likely due to the commonly know dry bias of RAOB.
  Comparisons of LVM with RAOBs shows larger std than spec. in upper troposphere; likely due to the lack of sounding information content in upper troposphere.

## Slide 72: Backup Material
GOES-19 ABI L2 LAP Product Provisional PS-PVR

## Slide 73: PLPT ABI-FD-TPW vs AMSR2:
73
Accuracy spec: 1 mm
Precision spec: 3 mm
number: 408379
bias: -1.67 mm
std: 2.01 mm
2024. 11 ~ 2024. 12
number: 415882
bias: -1.47 mm
std: 1.88 mm
GOES-16

## Slide 74: PLPT ABI-CONUS-TPW vs AMSR2:
74
Accuracy spec: 1 mm
Precision spec: 3 mm
number: 48381
bias: -2.06 mm
std: 2.33 mm
2024. 11 ~ 2024. 12
number: 46490
bias: -1.73 mm
std: 2.05 mm
GOES-16

## Slide 75: PLPT ABI-FD-TPW vs AMSR2:
75
Accuracy spec: 1 mm
Precision spec: 3 mm
number: 465796
bias: -1.78 mm
std: 2.42 mm
2024. 11 ~ 2024. 12
number: 466297
bias: -1.50 mm
std: 2.19 mm
GOES-18

## Slide 76: PLPT ABI-CONUS-TPW vs AMSR2:
76
Accuracy spec: 1 mm
Precision spec: 3 mm
number: 71176
bias: -1.10 mm
std: 2.05 mm
2024. 11 ~ 2024. 12
number: 67983
bias: -1.16 mm
std: 2.00 mm
GOES-18